## Slide 1: Sparse Matrix-Vector Multiply on the Texas Instruments C6678 Digital Signal Processor
Yang Gao and Dr. Jason D. Bakos
Application-Specific Systems, Architectures, and Processors 2013

## Slide 2: TI C6678 vs. Competing Coprocessors
Coprocessor | NVIDIA Tesla K20X GPU | Intel Xeon Phi 5110p | TI C66
Peak single precision performance | 3.95 Tflops/s | 2.12 Tflops/s | 128 Gflops/s
Memory bandwidth | 250 GB/s | 320 GB/s | 12.8 GB/s
Power | 225 W | 225 W | 10 W
Primary programming model | CUDA/OpenCL | OpenMP | None, but OpenMP/ OpenCL in development

## Slide 3: Why the C6678?
Unique architectural features
  8 symmetric VLIW cores with SIMD instructions, up to 16 flops/cycle
  No shared last level cache
  4MB on-chip shared RAM
  L1D and L2 can be configured as cache, scratchpad, or both
  DMA engine for parallel loading/flushing scratchpads
Power efficiency
  At 45 nm, achieves 12.8 ideal SP Gflops/Watt
  Intel Phi [22 nm] is 9.4 Gflops/Watt
  NVIDIA K20x [28 nm] is 17.6 Gflops/Watt
Fast on-chip interfaces for potential scalability
  4 x Rapid IO(SRIO) 2.1: 20 Gb/s
  1 x Ethernet: 1 Gb/s
  2 x PCI-E 2.0: 10 Gb/s
  HyperLink: 50 Gb/s

## Slide 4: C66 Platforms

## Slide 5: Software Pipelining
1
1
1
2
2
2
Time
Regular Loop
1
1
1
3
3
3
Software Pipelining
2
2
2
Prolog
Kernel
Epilog
ALU1
ALU2
ALU3
VLIW architecture requires explicit usage of functional units
C66 compiler uses software pipelining to maximize FU utilization
Conditional prevents SP and lowers utilization

## Slide 6: Sparse Matrices
We evaluated the C66 relative using a SpMV kernel
  GPUs achieve only 0.6% to 6% of their peak performance with CSR SpMV
Sparse Matrices can be very large but contain few non-zero elements
Compressed formats are often used, e.g. Compressed Sparse Row (CSR)
1 | -1 | 0 | -3 | 0
-2 | 5 | 0 | 0 | 0
0 | 0 | 4 | 6 | 4
-4 | 0 | 2 | 7 | 0
0 | 8 | 0 | 0 | -5
val | (1 | -1 | -3 | -2 | 5 | 4 | 6 | 4 | -4 | 2 | 7 | 8 | -5)
col | (0 | 1 | 3 | 0 | 1 | 2 | 3 | 4 | 0 | 2 | 3 | 1 | 4)
ptr | (0 | 3 | 5 | 8 | 11 | 13) |  |  |  |  |  |  | 

## Slide 7: Sparse Matrix-Vector Multiply
Code for y = Aax + by
  row = 0
  for i = 0 to number_of_nonzero_elements do
    if i == ptr[row+1] then row=row+1, y[row]*=beta;
    y[row] = y[row] + alpha * A[i] * x[col[i]]
  end
reduction
indirect indexing
Low arithmetic intensity
(~3 flops / 24 bytes)
Memory bound kernel
conditional execution

## Slide 8: Naïve Implementation
val
array
col
array
x array
if ptr[row] == i then
row = row +1
y[row]  y[row] * b
end if
y[row]y[row]+Acc
i
a * val * x
product results Acc
y buffer
ptr buffer
index
y write back
row
for i = columns assigned to current core
0.55 Gflops/s
60.4% of cycles were uncovered memory latency

## Slide 9: Double Buffer and DMA
val buffer
col buffer
x buffer
i
α * val * x
index
Product Loop
SDRAMbuffer
Val
L2 buffer
Col
L2 buffer
DMA
DSP
0.78 Gflops/s
28.8% of cycles were uncovered memory latency

## Slide 10: Loop Unroll and Predicate Instruction
Acc  Acc + prod[i]
if ptr[row] == i then
row = row +1
y[row]  y[row] * β
end if
y buffer
ptr buffer
y write back
row
i
prod buffer
Accumulate Loop
Acc  Acc + prod[i+1]
if ptr[row] == i then
row = row +1
y[row]  y[row] * β
end if
Acc  Acc + prod[i+K]
if ptr[row] == i then
row = row +1
y[row]  y[row] * β +Acc
end if
The accumulate loop is manually unrolled by 8
Predicate instructions are applied to replace the if-statements in assembly.
1.63 Gflops/s
50.1% cycles were uncovered memory latency

## Slide 11: Loop Fission
val buffer
col buffer
x buffer
Acc  Acc+prod[i]
if ptr[row] == i then
row = row +1
y[row]  y[row]*β+Acc
end if
i
α * val * x
product results
y buffer
ptr buffer
index
y write back
row
i
Product Loop
prod buffer
Accumulate Loop
2.08 Gflops/s
36.6% cycles were uncovered memory latency

## Slide 12: Adaptive Row Pointer
Acc  Acc + prod[i]
if ptr[row] == i then
row = row +1
y[row]  y[row] * β
end if
y buffer
ptr buffer
y write back
row
i
prod buffer
Accumulate Loop
Acc  Acc + prod[i+1]
if ptr[row] == i then
row = row +1
y[row]  y[row] * β
end if
Acc  Acc + prod[i+K]
if ptr[row] == i then
row = row +1
y[row]  y[row] * β
end if
Acc  Acc + prod[i]
Acc  Acc + prod[i+1]
…
Acc  Acc + prod[i+K]
if(ptr[row+1]-ptr[row]) >K

## Slide 13: Test Environment
 | i5 650 MKL | GTX680 CUSPARSE | GTX650Ti CUSPARSE | C66
Architecture | Clarkdale | Kepler | Kepler | Shannon
Process(nm) | 32 | 28 | 28 | 45
Memory throughput (GB/s) | 21 | 192.3 | 86.4 | 12.8
TDP (W) | 73 | 195 | 110 | 10
Single precision performance (Gflops) | 26 | 3090 | 1425 | 128

## Slide 14: Power Analyzer
PSU with EVM board
Power Socket Provide by WT500
110 V
12 V

## Slide 15: Matrix
Tri-diagonal
N-diagonal
3 - 501
University of Florida sparse matrix collection
Matrix Market
2, 4, 0, 0, 0, 0
5, 4, 7, 0, 0, 0
0, 6, 2, 4, 0, 0
0, 0, 3, 10, 1, 0
0, 0, 0, 4, 6, 8
0, 0, 0, 0, 2, 12

## Slide 16: SpMV Performance
N-diagonal Matrix
Generally, the C66 achieves ~2/3 CPU performance

## Slide 17: SpMV Gﬂops/Watt
N-diagonal Matrix
C66 is equivalent to GPUs when N > 51

## Slide 18: Gflops/Watt for Nonsynthetic Matrices
C66 power efficiency also scales with density for real-world matrices

## Slide 19: Memory Efficiency
N = 151
rows = 208326

## Slide 20: Memory Efficiency

## Slide 21: Next Generation
 | C66 | 66AK2H12 “Keystone-II”
CPU | n/a | 4 x ARM A15
DSP | 8 Cores | 8 Cores
DSP L2 | 512 KB | 1024 KB
DDR3 | 64 bit | 2 x 72 bit
Process | 45 nm | 28 nm
Power | 10 W | ?
Keystone-II
  28 nm
  Doubles caches
  Increases memory bandwidth by 125%

## Slide 22: Conclusions
TI DSP is a promising coprocessor technology for HPC
Advantages:
  Unique architectural features that facilitate automated parallelization (easier to program?)
  Inherently power efficient microarchitecture
    Equivalent to modern GPUs and Phi despite older process technology
  Has advanced memory system for memory bound kernels
    Simultaneous DMA and caching to match access pattern of indvidivual arrays
  Has advanced onchip interfaces for efficient scalability
    Large-scale multi-DSP platforms already exist
Looking forward:
  Keystone II will:
    Improve efficiency and memory performance (cache + b/w)
    Has onboard host CPUs to facilitate runtimes for multi-DSP scaling

## Slide 23: Q & A

## Slide 24: Arithmetic Intensity
val buffer
col buffer
x buffer
i
α * val * x
y buffer
ptr buffer
index
y write back
row
4 bytes
4 bytes
4/rows bytes
prod buffer
Acc  Acc+prod[i]
if ptr[row] == i then
row = row +1
y[row]  y[row]*β+Acc
end if
2 ops
1 op
4 bytes
4 bytes
4 bytes
2 ops
n = average number of non-zero elements per row