## Slide 1: OpenVX Graph Acceleration
Madushan Abeysinghe, Jesse Villarreal,
Lucas Weaver, Jason D. Bakos
Heterogeneous and Reconfigurable Computing Group

## Slide 2: TI C66 Digital Signal Processor
stage 0
stage 1
stage 0
for (i=0;i<n;i++) {
…
}
stage 2
stage 1
stage 0
stage 3
stage 2
stage 1
stage 0
stage 3
stage 2
stage 1
stage 3
stage 2
stage 3
execution flow
prolog
epilog
compiler
Circular buffer
Register file A
Register file B
Func. Unit 1A
Func. Unit 2A
Func. Unit 3A
Load/
Store A
Func. Unit 1B
Func. Unit 2B
Func. Unit 3B
Load/
Store B
ADD
MULT
ADD
NOP
MULT
ADD
NOP
NOP
LW
LW
NOP
NOP
LW
NOP
SW
NOP
VLIW
iteration internal

## Slide 3: OpenVX Framework
OpenVX is a standardized, cross platform framework to aid in development of accelerated computer vision, machine learning, and other signal processing applications.
OpenVX allows the programmer to define an application using a graph-based programming model
  Nodes: highly optimized kernels for the specific architecture
  Edges: represents data flow
Code-portable and Performance-portable !

## Slide 4: OpenVX/BAM on ADAS TDA2x
vxColorConvertNode
vxGaussian3x3Node
vxChannelExtractNode
OpenVX: pixel-by-pixel vision primitives

## Slide 5: OpenVX and BAM (current work)

## Slide 6: OpenVX and BAM (current work)
(process)
(in)
(out)

## Slide 7: DMA and Scratchpad
max(compute,DMA)
processor
DMA controller
trigger
time
idle
write tile n-1 to DRAM
process tile n
idle
input ping buffer
input pong buffer
output ping buffer
output pong buffer
tile n
tile n-1
tile n+1
tile n+2
tile n+1
read tile n+1 from DRAM
trigger
process tile n+1
idle
trigger
process tile n+2
idle
write tile n to DRAM
read tile n+2 from DRAM
idle
write tile n+1 to DRAM
tile n+1
tile n+2
tile n+1
tile n
tile n+2
tile n
tile n-1
tile n
tile n-1
tile n
tile n
tile n
tile n+1
tile n
max(trigger+compute,trigger+DMA)

## Slide 8: Performance Factor 1: Tile Size
Chart: AccumulateSquared Kernel 1600x1200 Input Image
| 32x16 | 32x24 | 64x16 | 64x24 | 64x48 | 64x64 | 128x48 | 256x24 | 320x24 | 384x16
DMA cycles | 4086042 | 3351592 | 2657840 | 2254197 | 2122940 | 2147923 | 1968607 | 2018998 | 1940477 | 2033277
Chart: AccumulateSquared Kernel 1600x1200 Input Image
| 32x16 | 32x24 | 64x16 | 64x24 | 64x48 | 64x64 | 128x48 | 256x24 | 320x24 | 384x16
DMA cycles | 4086042 | 3351592 | 2657840 | 2254197 | 2122940 | 2147923 | 1968607 | 2018998 | 1940477 | 2033277
Compute cycles | 2106936 | 1828958 | 1684803 | 1551327 | 1471052 | 1495759 | 1984855 | 2125456 | 2323605 | 2241750
1.58X
2.11X
best DMA
best compute
best max(DMA,compute)

## Slide 9: Performance Factor 2: Scratchpad Access Pattern
vxColorConvertNode
ex. time = X
vxGaussian3x3Node
ex. time = Z
vxChannelExtractNode
ex. time = Y
DRAM -> scratchpad (C)
DRAM -> scratchpad (A)
scratchpad -> DRAM (B)
scratchpad -> DRAM (D)
DRAM -> scatchpad (E)
scatchpad -> DRAM (F)
scratchpad buffers: 2, size = scratchpad/4
time = max(C+D,Y)

## Slide 10: Performance Factor 2: Scratchpad Access Pattern
vxColorConvertNode
ex. time = X
vxGaussian3x3Node
ex. time = Z
vxChannelExtractNode
ex. time = Y
scratchpad
DRAM -> scratchpad (A)
scratchpad
scratchpad -> DRAM (D)
DRAM -> scatchpad (E)
scatchpad -> DRAM (F)
scratchpad buffers: 3, size = scratchpad/6
time = max(A+D,(X+Y)/l)

## Slide 11: Lambda
l Values for Merged Kernels (Observed)

## Slide 12: Graph Partitioning
B6 = 203
B7 = 877
B8 = 4140
B9 = 21147
B10 = 115975
B11 = 678570
B12 = 4213597

## Slide 13: Performance Considerations
Problem:
  Group size determines:
    Number of DMA transactions
    Maximum tile size
    Lambda
  Tile size determines:
    DMA bandwidth
    Compute throughput
Approach:
  Train memory performance model and compute model to optimize grouping and tile size together

## Slide 14: DMA/Memory System Performance Model
Characterize:
  19 kernels (originally 35), 25 tile sizes, all possible pixel depths (per kernel)
  1460 total test cases (culled from 2819 original tests)
Features:
  input tile width, height in pixels (TIW, TIH)
  output tile width, height in pixels (TOW, TOH)
  total input, output width (tile width x pixel size x number of inputs) (TTIW, TTOW)
  total input, output size, TTIW*TIH (TIS, TOS)
  number of inputs, outputs (NI, NO)
  pixel depth (PD)
  stencil neighborhood width, height (SNW, SNH)
Best accuracy: TTIW, TIH, TTOW, TOH

## Slide 15: Performance Models
DMA: linear interpolant model of DMA b/w
  Find nearest 5 observations
    Calculate weights
    Calculate weighted average
  RMS training error = 32 MB/s
  RMS testing error = 248 MB/s
  Range = 189 MB/s to 4.33 GB/s
Compute: lookup kernel names and nearest tile WxH prod
616 MB/s
in_width=16,
out_width=8,
in_height=48,
out_height=48
in_width=16,
out_width=14,
in_height=48,
out_height=46
in_width=16,
out_width=10,
in_height=48,
out_height=42
in_width=16,
out_width=16,
in_height=48,
out_height=48
in_width=8,
out_width=8,
in_height=48,
out_height=48
in_width=8,
out_width=6,
in_height=48,
out_height=46
6.3
6.3
8.0
8.0
8.5
w=.23
w=.23
w=.18
w=.18
w=.17
723 MB/s
742 MB/s
423 MB/s
356 MB/s

## Slide 16: Lamdba Model
Lambda value depends on number of kernels and number of unique kernels
Used a piecewise interpolated model
  RMS error = 0.03 for training set of 43 test graphs
Lamdba vs graph size: same kernel
Lamdba vs graph size: unique kernels

## Slide 17: Model Accuracy and Performance
0.25 cycles/pixel (compute)
0.13 cycles/pixel
(compute)
0.44 cycles/pixel
(compute)
Compute bound:
0.81 cycles/pixel
DMA bound:
3 x 1600x1200x1 DMA @ 4.33 GB/s @ 750 MHz
0.48 cycles/pixel

## Slide 18: Impact of Tile Size on Merged Kernels
1.71

## Slide 19: Model Accuracy

## Slide 20: Model Accuracy

## Slide 21: Speedups
Comparison of Predicted and Real Speedups Speedups

## Slide 22: Randomly Generated Graphs
For each graph
  For each grouping
    For each allocable tile size (constrained by scratchpad capacity)…
      Find predicted speedup (vs individual nodes with 64x48 tiles)

## Slide 23: Speedup Distribution
Speedups above 1.5 = 0.95%
Speedups between 1 and 1.5 = 30.74%
Speedups below 1 = 68.30%

## Slide 24: Compute/DMA Makeup

## Slide 25: Conclusions
Performance models for DMA time and compute time for OpenVX graphs on C66 DSP
  Accurate to within ~10 to 15%
When used to automatically group random graphs, achieves a speedup of ~1.5 to 2
Future Work:
  Develep models to predict performance from merging the loops for each OpenVX kernel

## Slide 26: Thank you!
Questions?