## Slide 1: FPGA Acceleration of Phylogeny Reconstruction for Whole Genome Data
Jason D. Bakos
Panormitis E. Elenis
Jijun Tang
Dept. of Computer Science and Engineering
University of South Carolina
Columbia, SC USA

## Slide 2: Talk Outline
FPGAs and high-performance reconfigurable computing
Initial target application: gene rearrangement analysis
Hardware design and experimental results

## Slide 3: High-Performance Reconfigurable Computing
HPRC:
  Use FPGA as co-processor
Example:
  Application requires a week of CPU time
  One computation consumes 99% of execution time
Kernel speedup | Application speedup | Execution time
50 | 34 | 5.0 hours
100 | 50 | 3.3 hours
200 | 67 | 2.5 hours
500 | 83 | 2.0 hours
1000 | 91 | 1.8 hours
Replaces software
Exploits parallelism

## Slide 4: HPRC: Requirements, Pros, Cons
Application criteria:
  computationally expensive
  has a bottleneck computation
  bottleneck computation is parallelizable
  …and has low I/O and storage requirements
Advantages of HPRC:
  Cost
    FPGA card => ~ $15K
    128-processor cluster => ~ $150K
  + maintenance + cooling + electricity + recycling
Disadvantage for HPRC:
  Programming the FPGA

## Slide 5: Programming an FPGA
Requires large-scale digital logic design
  Instance and interconnect logic and memories
  Especially difficult for control-dependent computations
Even worse…
  To achieve performance:
    Finely parallelize algorithm across FPGA resources
Our solution:
  Develop a pre-designed library of kernels for computational biology
  Develop a design tool that uses this library to generate accelerators

## Slide 6: Talk Outline
FPGAs and high-performance reconfigurable computing
Initial target application: gene rearrangement analysis
Hardware design and experimental results

## Slide 7: Target Application
Gene rearrangement analysis
  Evolution analysis using gene order data
Assumes gene-rearrangement model for evolution, i.e.:
  Inversion
  g0 g1 g2 g3 g4 g5 g0 g1 –g4 –g3 –g2 g5
  Transposition
  g0 g1 g2 g3 g4 g5 g0 g2 g3 g4 g1 g5
  Transversion
  g0 g1 g2 g3 g4 g5 g0 –g4 –g3 –g2 g1 g5

## Slide 8: Reconstruction Method
Maximum parsimony:
  Search for tree with minimum number of rearrangement events
Direct-optimization method:
  To evaluate a fixed tree…
    Label all internal vertices with gene orders
      Initialize and iteratively refine until the labels converges
    Measure edge lengths using distance estimator
…
…
,
,

## Slide 9: Median
A
B
C
M
d(A,M)
d(B,M)
d(C,M)
Median computation used to label internal vertices
Find M that minimizes
d(A,M) + d(B,M) + d(C,M)
for some distance measure d()
For gene rearrangement data:
  Optimal solution is NP-hard in “diameter” of inputs:
  d(A,B) + d(A,C) + d(B,C)

## Slide 10: Execution Behavior
Evolution Rate of Inputs
Execution Time Ratio for Labeling
1
0
Application behavior depends on evolution rate of inputs
Execution time ratio for median computations:
  Asymptotically approaches 100% with diameter of input set
Median adopted as kernel computation

## Slide 11: Breakpoint Median
Construct a fully connected graph containing all g and –g for each gene
  w(g,-g) = -¥
  Initialize all other weights to be 3
  For each adjacency gh in the three genomes, decrement weight between vertex –g and h
Solve TSP
A = -1 +2 -4 -3
B = -1 -2 +3 +4
C = -2 +3 +4 +1
+
-
+
+
+
-
-
-
1
2
4
3
Edges not shown have cost = 3
cost = -¥
cost = 0
cost = 1
cost = 2
+
-
+
+
+
-
-
-
1
2
4
3
An optimal solution corresponding to genome +1 +2 -3 -4

## Slide 12: Breakpoint Median Algorithm
Optimal solution is feasible due to small graph
Algorithm:
  Represent TSP graph as a list of edges
  Test every possible valid combination of edges
Implemented as a branch-and-bound search
Upper bound is the best tour found so far
Lower bound is computed using a greedy algorithm
  Loop that inspects each vertex in TSP graph
  Accumulates lower bound value (based on search state)
  Performed each time an edge is added or deleted from solution state
  Requires nearly 100% of median execution time (bottleneck)

## Slide 13: Example Breakpoint Median
1 -1
2 -2
3 -3
4 -4
used
1 => 0
-1 => 0
2 => 0
-2 => 0
3 => 0
-3 => 0
4 => 0
-4 => 0
otherEnd
1 => -1
-1 => 1
2 => -2
-2 => 2
3 => -3
-3 => 3
4 => -4
-4 => 4
cost = 0
1 -1
2 -2
3 -3
4 -4
used
1 => 0
-1 => 0
2 => 0
-2 => 0
3 => 0
-3 => 1
4 => 1
-4 => 0
otherEnd
1 => -1
-1 => 1
2 => -2
-2 => 2
3 => -4
-3 => 3
4 => -4
-4 => 3
cost = 0
sorted edge list:
(-3,4,w=0)
(2,3,w=1)
(1,2,w=2)
(-1,-2,w=2)
(1,-2,w=2)
(-2,-4,w=2)
(-1,3,w=2)
(-1,-4,w=2)
(1,-4,w=2)
1 -1
2 -2
3 -3
4 -4
used
1 => 0
-1 => 0
2 => 1
-2 => 0
3 => 1
-3 => 1
4 => 1
-4 => 0
otherEnd
1 => -1
-1 => 1
2 => -2
-2 => -4
3 => -4
-3 => 3
4 => -4
-4 => -2
cost = 1
pruned

## Slide 14: Example Breakpoint Median
1 -1
2 -2
3 -3
4 -4
used
1 => 0
-1 => 0
2 => 0
-2 => 0
3 => 0
-3 => 0
4 => 0
-4 => 0
otherEnd
1 => -1
-1 => 1
2 => -2
-2 => 2
3 => -3
-3 => 3
4 => -4
-4 => 4
cost = 0
1 -1
2 -2
3 -3
4 -4
used
1 => 0
-1 => 0
2 => 0
-2 => 0
3 => 0
-3 => 1
4 => 1
-4 => 0
otherEnd
1 => -1
-1 => 1
2 => -2
-2 => 2
3 => -4
-3 => 3
4 => -4
-4 => 3
cost = 0
1 -1
2 -2
3 -3
4 -4
used
1 => 1
-1 => 0
2 => 1
-2 => 0
3 => 0
-3 => 1
4 => 1
-4 => 0
otherEnd
1 => -1
-1 => -2
2 => -2
-2 => -1
3 => -4
-3 => 3
4 => -4
-4 => 3
cost = 2
exclude edge (2,3)
1 -1
2 -2
3 -3
4 -4
used
1 => 1
-1 => 0
2 => 1
-2 => 1
3 => 0
-3 => 1
4 => 1
-4 => 1
otherEnd
1 => -1
-1 => 3
2 => -2
-2 => -1
3 => -1
-3 => 3
4 => -4
-4 => 3
cost = 4
1 -1
2 -2
3 -3
4 -4
used
1 => 1
-1 => 1
2 => 1
-2 => 1
3 => 1
-3 => 1
4 => 1
-4 => 1
otherEnd
1 => -1
-1 => 3
2 => -2
-2 => -1
3 => -1
-3 => 3
4 => -4
-4 => 3
cost = 6
tour is -1, 1, 2, -2, -4, 4, -3, 3
median is -1, 2, -4, -3
sorted edge list:
(-3,4,w=0)
(2,3,w=1)
(1,2,w=2)
(-1,-2,w=2)
(1,-2,w=2)
(-2,-4,w=2)
(-1,3,w=2)
(-1,-4,w=2)
(1,-4,w=2)

## Slide 15: Talk Outline
FPGAs and high-performance reconfigurable computing
Initial target application: gene rearrangement analysis
Hardware design and experimental results

## Slide 16: Hardware Median Core Design
Top-Level
Controller

## Slide 17: Parallelizing the Median Computation
Exploit both fine- and coarse- grain parallelism
Fine-grain
  Unroll loop for lower bound computation
  Perform multiple iterations in parallel
Coarse-grain
  Use parallel median cores for single median computation
  Partition search space

## Slide 18: Fine-Grain Parallelism
1 (1,-4),w=0
-1 (-1,9),w=1 (-1,25),w=2
2 (2,11),w=2 (2,-19),w=2 (2,-49),w=2
-2 (-2,17),w=2 (-2,20),w=1
.
.
.
-19 (-19,2),w=2 (-19,-4),w=2 (-19,10),w=2
.
.
.
used
table
v=2
e0=11
e1=-19
e2=-49
TSP graph representation:
otherEnd
table
v=2
excluded
table
v=2
if used(v) = 0 then
VALID_WEIGHTS= f
for i = 0 to edge_count(v) - 1
if used(ei) = 0 and
otherEnd(v) != ei and
excludedi(v) != 1 then
add weighti to VALID_WEIGHTS
end if
end loop
if VALID_WEIGHTS is empty
lower_bound = lower_bound + 3
else
lower_bound = min(VALID_WEIGHTS)
end if
used(v)
used(e0)
used(e1)
used(e2)
otherEnd(v)
excluded0(v)
excluded1(v)
excluded2(v)
edge_count
table
v=2
3
2
11
-49
-19
weight0
weight1
weight2
2
2
2
Lower bound unit:
2
2
2

## Slide 19: Coarse-Grain Parallelism
Parallelize search => partition TSP search space
  Problems:
    High amount of state information (communication overhead)
    Dynamic load balancing would be complex (control overhead)
Solution: “virtually” partition the TSP search space
  Search order determined by ordering of edge list
  Use parallel median cores
  Each core uses unique search order
  All cores share a global upper bound value

## Slide 20: Experimental Results: Median Acceleration
Best performance was achieved:
  20 lower bound units per core
  2 cores
  ~ 50% of FPGA resources
Performance improves with size of search space
  i.e. search time
  Host-FPGA communication overhead
Average speedup for 1000 median computations

## Slide 21: Experimental Results: Application Acceleration
Perform end-to-end reconstruction procedure
Dispatch all median computations to FPGA
Average speedup for 10 end-to-end reconstructions

## Slide 22: Conclusions and Future Work
Achieved 100X end-to-end application speedup for distantly related data sets
Demonstrated that FPGAs can accelerate this class of application
Future Work:
  Additional kernel designs (i.e. tree generation)
  Implement heterogeneous mix of kernels on the FPGA according to evolution rate of input set