## Slide 1: Trends in the Infrastructure of Computing: Processing, Storage, Bandwidth
CSCE 190: Computing in the Modern World
Dr. Jason D. Bakos

## Slide 2: Lecture Outline
Introduction
  Digital integrated circuits: from silicon to microprocessors
Trends in processing
  Increasing microprocesor speed
  Microarchitectural parallelism
  High-performance computing
  High-performance reconfigurable computing
Trends in bandwidth
  Interconnects
  Networks
Trends in storage

## Slide 3: Elements

## Slide 4: Semiconductors
Silicon is a group IV element (4 valence electrons, shells: 2, 8, 18, 32…)
  Forms covalent bonds with four neighbor atoms (3D cubic crystal lattice)
  Si is a poor conductor, but conduction characteristics may be altered
  Add impurities/dopants (replaces silicon atom in lattice):
    Makes a better conductor
    Group V element (phosphorus/arsenic) => 5 valence electrons
      Leaves an electron free => n-type semiconductor (electrons, negative carriers)
    Group III element (boron) => 3 valence electrons
      Borrows an electron from neighbor => p-type semiconductor (holes, positive carriers)
forward bias
reverse bias
+ + +
+ + +
- - -
- - -
P-N junction
+
-
-
+
+ + +
+ + +
- - -
- - -

## Slide 5: MOSFETs
body/bulk
GROUND
NMOS/NFET
PMOS/PFET
channel
shorter length, faster transistor (dist. for electrons)
body/bulk
HIGH
positive voltage (Vdd)
negative voltage (rel. to body) (GND)
(S/D to body is reverse-biased)
- - -
+ + +
+ + +
- - -
current
current
Metal-poly-Oxide-Semiconductor structures built onto substrate
  Diffusion: Inject dopants into substrate
  Oxidation: Form layer of SiO2 (glass)
  Deposition and etching: Add aluminum/copper wires

## Slide 6: Logic Gates
inv
NAND2
NAND3
NOR2

## Slide 7: Latches
Positive edge-sensitive latch

## Slide 8: IC Fabrication
Inverter cross-section
field oxide

## Slide 9: IC Fabrication
Chips are fabricated using set of masks
  Photolithography
Inverter uses 6 layers:
  n-well, poly, n+ diffusion, p+ diffusion, contact, metal
Basic steps
  oxidize
  apply photoresist
  remove photoresist with mask
  HF acid eats oxide but not photoresist
  pirana acid eats photoresist
  ion implantation (diffusion, wells)
  vapor deposition (poly)
  plasma etching (metal)

## Slide 10: IC Fabrication
Furnace used to oxidize (900-1200 C)
Mask exposes photoresist to light, allowing removal
HF acid etch
piranha acid etch
diffusion (gas) or ion implantation (electric field)
HF acid etch

## Slide 11: IC Fabrication
Heavy doped poly is grown with gas in furnace (chemical vapor deposition)
Masked used to pattern poly
Poly is not affected by ion implantation

## Slide 12: IC Fabrication
Metal is sputtered (with vapor) and plasma etched from mask

## Slide 13: Layout
3-input NAND

## Slide 14: Cell Library (Snap Together)
Layout

## Slide 15: Logic Synthesis
Behavior:
  S = A + B
  Assume A is 2 bits, B is 2 bits, C is 3 bits
A | B | C
00 (0) | 00 (0) | 000 (0)
00 (0) | 01 (1) | 001 (1)
00 (0) | 10 (2) | 010 (2)
00 (0) | 11 (3) | 011 (3)
01 (1) | 00 (0) | 001 (1)
01 (1) | 01 (1) | 010 (2)
01 (1) | 10 (2) | 011 (3)
01 (1) | 11 (3) | 100 (4)
10 (2) | 00 (0) | 010 (2)
10 (2) | 01 (1) | 011 (3)
10 (2) | 10 (2) | 100 (4)
10 (2) | 11 (3) | 101 (5)
11 (3) | 00 (0) | 011 (3)
11 (3) | 01 (1) | 100 (4)
11 (3) | 10 (2) | 101 (5)
11 (3) | 11 (3) | 110 (6)

## Slide 16: MIPS Microarchitecture

## Slide 17: Synthesized and P&R’ed MIPS Architecture

## Slide 18: Lecture Outline
Introduction
  Digital integrated circuits: from silicon to microprocessors
Trends in processing
  Increasing microprocesor speed
  Microarchitectural parallelism
  High-performance computing
  High-performance reconfigurable computing
Trends in bandwidth
  Interconnects
  Networks
Trends in storage

## Slide 19: Feature Size
Shrink minimum feature size…
  Smaller L decreases carrier time and increases current
  Therefore, W may also be reduced for fixed current
  Cg, Cs, and Cd are reduced
  Transistor switches faster (~linear relationship)

## Slide 20: Minimum Feature Size
Year | Processor | Speed | Process
1982 | i286 | 6 - 25 MHz | 1.5 mm
1986 | i386 | 16 – 40 MHz | 1.5 - 1 mm
1989 | i486 | 16 - 133 MHz | .8 mm
1993 | Pentium | 60 - 300 MHz | .6 - .25 mm
1995 | Pentium Pro | 150 - 200 MHz | .5 - .35 mm
1997 | Pentium II | 233 - 450 MHz | .35 - .25 mm
1999 | Pentium III | 450 – 1400 MHz | .25 - .13 mm
2000 | Pentium 4 | 1.3 – 3.8 GHz | .18 - .065 mm
2005 | Pentium D | 2.66 – 3.6 GHz | .09 - .065 mm
2006 | Core 2 | 1.06 – 3 GHz | .065 mm
Upcoming milestones:
45 nm (Xeon 5400 Nov. 2007),
32 nm (2009-2010), 22 nm (2011-2012), 16 nm (2013)

## Slide 21: Clock Speed
“Megahertz myth”:
  In the late 1990’s and early 2000’s, the marketing arm of microprocessor companys overstated the corralation between clock speed and performance
Execution time =
  instructions per program * cycles per instruction * seconds per cycle
Now we must add to the product:
  (number of threads / number of cores)

## Slide 22: Integration Density Trends (Moore’s Law)
Pentium Core 2 Duo (2007) has ~300M transistors

## Slide 23: Microprocessor Technology
Advances in fabrication (lithography, photoresist, metal layers)
…faster transistor switching (faster processor)
…smaller transistors/wires
…higher integration density
…more “real estate”
…architectural improvements!

## Slide 24: Instruction Set Architecture
Example:
  Motorola 6800 / Intel 8085 (1970s)
    1-address architecture: ADDA <mem_addr>
    (A) = (A) + (addr)
  Intel x86 / IBM 360 (1980s)
    2-address architecture: ADD EAX, EBX –or- ADD EAX,<mem_addr>
    (A) = (A) + (B)
  MIPS (1990s)
    3-address architecture: ADD $2, $3, $4
    ($2) = ($3) + ($4)
  Instruction-level Parallelism (2000s)

## Slide 25: Machine Code Example
for (i=0;i<n;i++) a[i]=b[i]+10;
xor $2,$2,$2 # zero out index register (i)
lw $3,n # load iteration limit
sll $3,$3,2 # multiply by 4 (words)
la $4,a # get address of a (assume < 216)
la $5,b # get address of b (assume < 216)
j test
loop: add $6,$5,$2 # compute address of b[i]
lw $7,0($6) # load b[i]
addi $7,$7,10 # compute b[i]=b[i]+10
add $6,$4,$2 # compute address of a[i]
sw $7,0($6) # store into a[i]
addi $2,$2,4 # increment i
test: blt $2,$3,loop # loop if test succeeds

## Slide 26: Microarchitectural Parallelism
Parallelism => perform multiple operations simultaneously
  Instruction-level parallelism
    Execute multiple instructions at the same time
    Multiple issue
    Out-of-order execution
    Speculation
  Thread-level parallelism (hyper-threading)
    Execute multiple threads at the same time on one CPU
    Threads share memory space and pool of functional units
  Chip multiprocessing
    Execute multiple processes/threads at the same time on multiple CPUs
    Cores are symmetrical and completely independent but share a common level-2 cache

## Slide 27: Parallel Processing
Parallel processing:
  Shared memory
    Symmetric multiprocessing
    Multiple CPUs share a single memory space (usually NUMA)
    Communicate through memory reference
    Each CPU may have local but globally accessible memory
    Requires expensive crossbar switch (16-processor => $500K)
  Message-passing
    No shared memory
    CPUs communicate via explicit messages
    MPI and OpenMP APIs
    COTS processors and high-speed LAN switch
    Scalable:
      NASA Space Exploration Simulator has 10,240 CPUs (Intel Itanium 2) and requires 1 MW (Lake Murray generates 200 MW)
      Laurence Livermore BlueGene/L has 65,536 dual-processor (700 MHz PowerPC) nodes and requires 1.5 MW
  Hybrid systems

## Slide 28: High-Performance Reconfigurable Computing
HPRC:
  Use FPGA as co-processor
Example:
  Application requires a week of CPU time
  One computation consumes 99% of execution time
Kernel speedup | Application speedup | Execution time
50 | 34 | 5.0 hours
100 | 50 | 3.3 hours
200 | 67 | 2.5 hours
500 | 83 | 2.0 hours
1000 | 91 | 1.8 hours
Replaces software
Exploits parallelism

## Slide 29: HPRC: Requirements, Pros, Cons
Application criteria:
  computationally expensive
  has a bottleneck computation
  bottleneck computation is parallelizable
  …and has low I/O and storage requirements
Advantages of HPRC:
  Cost
    FPGA card => ~ $15K
    128-processor cluster => ~ $150K
  + maintenance + cooling + electricity + recycling
Disadvantage for HPRC:
  Programming the FPGA

## Slide 30: Lecture Outline
Introduction
  Digital integrated circuits: from silicon to microprocessors
Trends in processing
  Increasing microprocesor speed
  Microarchitectural parallelism
  High-performance computing
  High-performance reconfigurable computing
Trends in bandwidth
  Interconnects
  Networks
Trends in storage

## Slide 31: Interconnects
On-chip
Printed circuit boards
Multi-Chip Module
Backplanes
Peripherals
Pentium Core Duo
128 single-ended wires @ 8 Gbps/wire = 1024 Gbps
DVD in .04 s
Pentium D
64 single-ended wires @ 4 Gbps/wire = 256 Gbps
DVD in .15 s
Processor to RAM
32 single-ended wires @ 2 Gbps/wire = 64 Gbps
DVD in .6 s
PCIe
16 differential channels @ 2 Gbps/ch = 32 Gbps
DVD in 1.2 s
SATA
1 bi-directional differential channel @ 3 Gbps/ch
DVD in 12.6 s
1394b
1 bi-directional differential channel @ .8 Gbps/ch
DVD in 47 s
USB 2.0
1 bi-directional differential channel @ .4 Gbps/ch
DVD in 94 s
Notes:
Peripheral and LAN interconnects have “marketing speeds” which typically do not consider phyical layer overhead and usually aggregate parallel and bidirectional channels!

## Slide 32: Challenges for System-Level Interconnects
Signal integrity
  RLC effects
  Noise (switching, RF, etc.)
  Crosstalk
  Synchronization/jitter/skew
  Skin effect
  Dielectric loss
  Signal reflection
Area
  I/O pads precious
  Driver size
Packaged chip
Packaged chip
Source: Intel Corporation

## Slide 33: Multi-Bit Differential Signaling (MBDS)
Differential (LVDS) channels
Data encoded as
  {01} or {10}
Advantages
  Low switching noise
  Large GDP
  Common-mode noise rejection
  EM coupled transmission lines
  Low noise => low voltage swing
Disadvantages
  Wasteful in I/O pads
Single-ended channels
Data generally not encoded but can be modulated
  i.e. pulse amplitude modulation (RAMBUS)

## Slide 34: Multi-Bit Differential Signaling (MBDS)
Differential (LVDS) channels
Data encoded as
  {01} or {10}
Advantages
  Low switching noise
  Large GDP
  Common-mode noise rejection
  EM coupled transmission lines
  Low noise => low voltage swing
Disadvantages
  Wasteful in I/O pads
Multi-Bit Differential (MBDS) channel
Scale up LVDS driver
Data encoded with fixed number of ones
“N-choose-M (nCm)” symbols
  {0011}, {0101}, {0110}, {1001}, {1010}, {1100}
Advantages
  Same transmission characteristics as differential
  Higher information capacity

## Slide 35: OE Conversion Technology
Area pads
Window
VCSEL site
Passive alignment mark
Assembled OE-chip
SoS die

## Slide 36: OE Crossbar Switch Chip
64 optical channels
8x8 at 250 mm pitch (1.75 x 1.75 mm)
~ 3 Gbps / channel => 192 Gbps

## Slide 37: OE Interconnect using Fiber Image Guides
Top
Bottom
Side
Dense lattice of fiber cores
5-20 um diameter, 2K-15K cores/mm2

## Slide 38: OE-MCM Demonstrator
Chip 2
Chip 3
Chip 1
Chip 2
Chip 3
IN
OUT
Chip 1

## Slide 39: LANs
Peripheral and LAN switched interconnects are merging
LAN
  Fibre Channel
    For storage devices / SAN (1 – 12.75 Gbps)
    16 port 1U 2.12 Gbps is $15K
  Infiniband (copper or fiber)
    2.5 Gbps
    16 port is $10K
  Myrinet (designed for clusters)
    10 Gbps
    16 port for $10K
  1G/10G Ethernet

## Slide 40: WANs
WAN
  SONET
    Synchronous optical networking
    1 frame is transmitted every 125 ms (8 KHz)
    Frame size depends on line speed:
      OC-1 ~ 51.8 Mbps, frame size = 810 bytes
      OC-48 ~ 2.5 Gbps (regional ISP backbone)
      OC-192 ~ 10 Gbps (fastest backbone connection currently in use)
      OC-768 ~ 40 Gbps (2007 -- short range only), interfaces include four Xilinx FPGAs
      OC-1536 ~ 80 Gbps (no standards yet)
      OC-3072 ~ 160 Gbps (no standards yet)

## Slide 41: Lecture Outline
Introduction
  Digital integrated circuits: from silicon to microprocessors
Trends in processing
  Increasing microprocesor speed
  Microarchitectural parallelism
  High-performance computing
  High-performance reconfigurable computing
Trends in bandwidth
  Interconnects
  Networks
Trends in storage

## Slide 42: Memory

## Slide 43: Array Architecture

## Slide 44: SRAM
Static RAM cell
Reads:
  bitlines are precharged high
  one is pulled down by cell
  sense amplifiers read small differences
Writes:
  bitline or its complement are driven low
Challenge:
  decoding

## Slide 45: DRAM
Stores contents as charge on capacitor
Read:
  bitline is pre-charged to Vdd/2
  wordline raises, causing voltage change
  value is re-written
Write:
  bitline driven high or low

## Slide 46: Flash Memory
Use floating gate and avalanche injection

## Slide 47: Flash Technology
NOR ROM
  fast
NAND ROM
  dense but slow

## Slide 48: Flash RAM
Solid-state disks (Slashdot)
  Samsung announced 64 Gb (8GB) NAND flash chip w/30nm process
  Opens the door for 128GB flash cards