## Slide 1: Trends in the Infrastructure of Computing: Processing, Storage, Bandwidth
CSCE 190: Computing in the Modern World
Dr. Jason D. Bakos

## Slide 2: Elements

## Slide 3: Semiconductors
Silicon is a group IV element (4 valence electrons, shells: 2, 8, 18, 32…)
  Forms covalent bonds with four neighbor atoms (3D cubic crystal lattice)
  Si is a poor conductor, but conduction characteristics may be altered
  Add impurities/dopants (replaces silicon atom in lattice):
    Makes a better conductor
    Group V element (phosphorus/arsenic) => 5 valence electrons
      Leaves an electron free => n-type semiconductor (electrons, negative carriers)
    Group III element (boron) => 3 valence electrons
      Borrows an electron from neighbor => p-type semiconductor (holes, positive carriers)
forward bias
reverse bias
+ + +
+ + +
- - -
- - -
P-N junction
+
-
-
+
+ + +
+ + +
- - -
- - -
Spacing=543 pm

## Slide 4: MOSFETs
body/bulk
GROUND
NMOS/NFET
PMOS/PFET
channel
shorter length, faster transistor (dist. for electrons)
body/bulk
HIGH
positive voltage (Vdd)
negative voltage (rel. to body) (GND)
(S/D to body is reverse-biased)
- - -
+ + +
+ + +
- - -
current
current
Metal-poly-Oxide-Semiconductor structures built onto substrate
  Diffusion: Inject dopants into substrate
  Oxidation: Form layer of SiO2 (glass)
  Deposition and etching: Add aluminum/copper wires

## Slide 5: Layout
3-input NAND

## Slide 6: Logic Gates
inv
NAND2
NAND3
NOR2

## Slide 7: Logic Synthesis
Behavior:
  S = A + B
  Assume A is 2 bits, B is 2 bits, C is 3 bits
A | B | C
00 (0) | 00 (0) | 000 (0)
00 (0) | 01 (1) | 001 (1)
00 (0) | 10 (2) | 010 (2)
00 (0) | 11 (3) | 011 (3)
01 (1) | 00 (0) | 001 (1)
01 (1) | 01 (1) | 010 (2)
01 (1) | 10 (2) | 011 (3)
01 (1) | 11 (3) | 100 (4)
10 (2) | 00 (0) | 010 (2)
10 (2) | 01 (1) | 011 (3)
10 (2) | 10 (2) | 100 (4)
10 (2) | 11 (3) | 101 (5)
11 (3) | 00 (0) | 011 (3)
11 (3) | 01 (1) | 100 (4)
11 (3) | 10 (2) | 101 (5)
11 (3) | 11 (3) | 110 (6)

## Slide 8: MIPS Microarchitecture

## Slide 9: Synthesized and P&R’ed MIPS Architecture

## Slide 10: Feature Size
Shrink minimum feature size…
  Smaller L decreases carrier time and increases current
  Therefore, W may also be reduced for fixed current
  Cg, Cs, and Cd are reduced
  Transistor switches faster (~linear relationship)

## Slide 11: Minimum Feature Size
Year | Processor | Speed | Transistors | Process
1982 | i286 | 6 - 25 MHz | ~134,000 | 1.5 mm
1986 | i386 | 16 – 40 MHz | ~270,000 | 1 mm
1989 | i486 | 16 - 133 MHz | ~1 million | .8 mm
1993 | Pentium | 60 - 300 MHz | ~3 million | .6 mm
1995 | Pentium Pro | 150 - 200 MHz | ~4 million | .5 mm
1997 | Pentium II | 233 - 450 MHz | ~5 million | .35 mm
1999 | Pentium III | 450 – 1400 MHz | ~10 million | .25 mm
2000 | Pentium 4 | 1.3 – 3.8 GHz | ~50 million | .18 mm
2005 | Pentium D | 2 cores/package | ~200 million | .09 mm
2006 | Core 2 | 2 cores/die | ~300 million | .065 mm
2008 | Core i7 | 4 cores/die | ~800 million | .045 mm
2010 | “Sandy Bridge” | 8 cores/die | ?? | .032 mm

## Slide 12: Real Estate

## Slide 13: Heterogeneous Computing: Execution Model
initialization
0.5% of run time
“hot” loop
99% of run time
clean up
0.5% of run time
instructions executed over time
49% of code
49% of code
1% of code
co-processor

## Slide 14: Co-Processor Design
FPGA design:

## Slide 15: HC Execution Model
CPU
X58
Host Memory
Co-processor
QPI
PCIe
On board
Memory
add-in card
host
In general, co-processor can achieve 10x – 1000x computational throughput vs. CPU
Pay penaly for transferring memory between host memory and on-board memory
Add-in card can have arbitrary amount of memory bandwidth (use proprietray memory interface)
~25 GB/s
~25 GB/s
~8 GB/s (x16)
?????
~100 GB/s for GeForce 260

## Slide 16: HC Execution Model

## Slide 17: Heterogeneous Computing: Performance
Example:
  Application requires a week of CPU time
  One computation consumes 99% of execution time
Kernel speedup | Application speedup | Execution time
50 | 34 | 5.0 hours
100 | 50 | 3.3 hours
200 | 67 | 2.5 hours
500 | 83 | 2.0 hours
1000 | 91 | 1.8 hours

## Slide 18: Heterogeneous Computing with FPGAs

## Slide 19: Programming FPGAs

## Slide 20: Heterogeneous Computing with GPUs
Graphics Processor Unit (GPU)
  Contains hundreds of small processor cores grouped hierarchically
  Has high bandwidth to on-board memory and to host memory
  Became “programmable” about two years ago
  Gained hardware double precision about one year ago
Examples: IBM Cell, nVidia GeForce, AMD FireStream
Advantage over FPGAs:
  Easier to program
  Less expensive (gamers drove high volumes, decreasing cost)
Drawbacks:
  Can’t necessarily outperform FPGAs for all types of computations
    Characterizing this is an open research problem

## Slide 21: NVIDIA GPU Architecture

## Slide 22: IBM Cell Architecture

## Slide 23: Heterogeneous Computing now Mainstream: IBM Roadrunner
Los Alamos, fastest computer in the world
6,480 AMD Opteron (dual core) CPUs
12,960 PowerXCell 8i GPUs
Each blade contains 2 Operons and 4 Cells
296 racks
1.71 petaflops peak (1.7 billion million fp operations per second)
2.35 MW (not including cooling)
  Lake Murray hydroelectric plant produces ~150 MW (peak)
  Lake Murray coal plant (McMeekin Station) produces ~300 MW (peak)
  Catawba Nuclear Station near Rock Hill produces 2258 MW

## Slide 24: Our Group
Past projects:
  Custom FPGA accelerators and components:
    computational biology
    linear algebra
  Multi-FPGA interconnection networks:
    interface abstractions
    adaptive routing algorithms
    on-chip router designs
Current projects:
  Design tools
    Dynamic code analysis
    Semi-automatic accelerator generation
  GPU simulation and emulation for code tuning