## Slide 1: Trends in the Infrastructure of Computing: Processing, Storage, Bandwidth
CSCE 190: Computing in the Modern World
Dr. Jason D. Bakos

## Slide 2: Elements

## Slide 3: Semiconductors
Silicon is a group IV element (4 valence electrons, shells: 2, 8, 18, 32…)
  Forms covalent bonds with four neighbor atoms (3D cubic crystal lattice)
  Si is a poor conductor, but conduction characteristics may be altered
  Add impurities/dopants (replaces silicon atom in lattice):
    Makes a better conductor
    Group V element (phosphorus/arsenic) => 5 valence electrons
      Leaves an electron free => n-type semiconductor (electrons, negative carriers)
    Group III element (boron) => 3 valence electrons
      Borrows an electron from neighbor => p-type semiconductor (holes, positive carriers)
forward bias
reverse bias
+ + +
+ + +
- - -
- - -
P-N junction
+
-
-
+
+ + +
+ + +
- - -
- - -
Spacing=543 pm

## Slide 4: MOSFETs
body/bulk
GROUND
NMOS/NFET
PMOS/PFET
channel
shorter length, faster transistor (dist. for electrons)
body/bulk
HIGH
positive voltage (Vdd)
negative voltage (rel. to body) (GND)
(S/D to body is reverse-biased)
- - -
+ + +
+ + +
- - -
current
current
Metal-poly-Oxide-Semiconductor structures built onto substrate
  Diffusion: Inject dopants into substrate
  Oxidation: Form layer of SiO2 (glass)
  Deposition and etching: Add aluminum/copper wires

## Slide 5: Layout
3-input NAND

## Slide 6: Logic Gates
inv
NAND2
NAND3
NOR2

## Slide 7: Logic Synthesis
Behavior:
  S = A + B
  Assume A is 2 bits, B is 2 bits, C is 3 bits
A | B | C
00 (0) | 00 (0) | 000 (0)
00 (0) | 01 (1) | 001 (1)
00 (0) | 10 (2) | 010 (2)
00 (0) | 11 (3) | 011 (3)
01 (1) | 00 (0) | 001 (1)
01 (1) | 01 (1) | 010 (2)
01 (1) | 10 (2) | 011 (3)
01 (1) | 11 (3) | 100 (4)
10 (2) | 00 (0) | 010 (2)
10 (2) | 01 (1) | 011 (3)
10 (2) | 10 (2) | 100 (4)
10 (2) | 11 (3) | 101 (5)
11 (3) | 00 (0) | 011 (3)
11 (3) | 01 (1) | 100 (4)
11 (3) | 10 (2) | 101 (5)
11 (3) | 11 (3) | 110 (6)

## Slide 8: Microarchitecture

## Slide 9: Synthesized and P&R’ed MIPS Architecture

## Slide 10: Feature Size
Shrink minimum feature size…
  Smaller L decreases carrier time and increases current
  Therefore, W may also be reduced for fixed current
  Cg, Cs, and Cd are reduced
  Transistor switches faster (~linear relationship)

## Slide 11: Minimum Feature Size
Year | Processor | Speed | Transistor Size | Transistors
1982 | i286 | 6 - 25 MHz | 1.5 mm | ~134,000
1986 | i386 | 16 – 40 MHz | 1 mm | ~270,000
1989 | i486 | 16 - 133 MHz | .8 mm | ~1 million
1993 | Pentium | 60 - 300 MHz | .6 mm | ~3 million
1995 | Pentium Pro | 150 - 200 MHz | .5 mm | ~4 million
1997 | Pentium II | 233 - 450 MHz | .35 mm | ~5 million
1999 | Pentium III | 450 – 1400 MHz | .25 mm | ~10 million
2000 | Pentium 4 | 1.3 – 3.8 GHz | .18 mm | ~50 million
2005 | Pentium D | 2 threads/package | .09 mm | ~200 million
2006 | Core 2 | 2 threads/die | .065 mm | ~300 million
2008 | Core i7 “Nehalem” | 8 threads/die | .045 mm | ~800 million
2011 | “Sandy Bridge” | 16 threads/die | .032 mm | ~1.2 billion
Year | Processor | Speed | Transistor Size | Transistors
2008 | NVIDIA Tesla | 240 threads/die | .065 mm | 1.4 billion
2010 | NVIDIA Fermi | 512 threads/die | .040 mm | 3 billion

## Slide 12: CPU Design
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Control
L1 cache
L2 cache
Control
L1 cache
L2 cache
L3 cache
CPU
Core 1
Core 2
FOR i = 1 to 1000
C[i] = A[i] + B[i]
Copy part of A onto CPU
Copy part of B onto CPU
ADD
ADD
ADD
ADD
Copy part of C into Mem
time
Copy part of A onto CPU
Copy part of B onto CPU
ADD
ADD
ADD
ADD
Copy part of C into Mem
…

## Slide 13: Co-Processor Design
ALU
ALU
ALU
ALU
cache
GPU
Core 1
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
Core 2
Core 3
Core 4
Core 5
Core 6
Core 7
Core 8
FOR i = 1 to 1000
C[i] = A[i] + B[i]

## Slide 14: Heterogeneous Computing
CPU
X58
Host Memory
Co-processor
QPI
PCIe
On board
Memory
add-in card
host
General purpose CPU + special-purpose processors in one system
~25 GB/s
~25 GB/s
~8 GB/s (x16)
?????
~150 GB/s for GeForce 260
System I/O controller

## Slide 15: Heterogeneous Computing
initialization
0.5% of run time
“hot” loop
99% of run time
clean up
0.5% of run time
49% of code
49% of code
2% of code
co-processor
Kernel speedup | Application speedup | Execution time
50 | 34 | 5.0 hours
100 | 50 | 3.3 hours
200 | 67 | 2.5 hours
500 | 83 | 2.0 hours
1000 | 91 | 1.8 hours
Combine CPUs and coprocs
Example:
  Application requires a week of CPU time
  Offload computation consumes 99% of execution time

## Slide 16: NVIDIA GPU Architecture
Hundreds of simple processor cores
Core design:
  Only one instruction from each thread active in the pipeline at a time
  In-order execution
  No branch prediction
  No speculative execution
  No support for context switches
  No system support (syscalls, etc.)
  Small, simple caches
  Programmer-managed on-chip scratch memory

## Slide 17: Programming GPUs
HOST (CPU) code:
dim3 grid,block;
grid.x=((VECTOR_SIZE/512) + (VECTOR_SIZE%512?1:0));
block.x=512;
cudaMemcpy(a_device,a,VECTOR_SIZE * sizeof(double),cudaMemcpyHostToDevice);
cudaMemcpy(b_device,b,VECTOR_SIZE * sizeof(double),cudaMemcpyHostToDevice);
vector_add_device<<<grid,block>>>(a_device,b_device,c_device);
cudaMemcpy(c_gpu,c_device,VECTOR_SIZE * sizeof(double),cudaMemcpyDeviceToHost);
GPU code:
__global__ void vector_add_device (double *a,double *b,double *c) {
__shared__ double a_s,b_s,c_s;
a_s=a[blockIdx.x*blockDim.x+threadIdx.x];
b_s=b[blockIdx.x*blockDim.x+threadIdx.x];
c_s=a_s+b_s;
c[blockIdx.x*blockDim.x+threadIdx.x]=c_s;
}

## Slide 18: IBM Cell/B.E. Architecture
1 PPE, 8 SPEs
Programmer must manually manage 256K memory and threads invocation on each SPE
Each SPE includes a vector unit like the one on current Intel processors
  128 bits wide

## Slide 19: High-Performance Reconfigurable Computing
Heterogeneous computing with reconfigurable logic, i.e. FPGAs

## Slide 20: Field Programmable Gate Arrays

## Slide 21: Heterogeneous Computing with FPGAs

## Slide 22: Programming FPGAs

## Slide 23: Heterogeneous Computing with FPGAs
Annapolis Micro Systems
WILDSTAR 2 PRO
GiDEL PROCSTAR III

## Slide 24: Heterogeneous Computing with FPGAs
Convey HC-1

## Slide 25: Heterogeneous Computing with GPUs
NVIDIA Tesla S1070

## Slide 26: Heterogeneous Computing now Mainstream: IBM Roadrunner
Los Alamos, fastest computer in the world in 2008 (still in Top 10)
6,480 AMD Opteron (dual core) CPUs
12,960 PowerXCell 8i GPUs
Each blade contains 2 Operons and 4 Cells
296 racks
First ever petaflop machine (2008)
1.71 petaflops peak (1.7 billion million fp operations per second)
2.35 MW (not including cooling)
  Lake Murray hydroelectric plant produces ~150 MW (peak)
  Lake Murray coal plant (McMeekin Station) produces ~300 MW (peak)
  Catawba Nuclear Station near Rock Hill produces 2258 MW

## Slide 27: Conclusion
Even though integration levels continue to increase exponentially, processor makers still need to budget their real estate to target specific application targets
Use of heterogeneous computing is on the rise for both high performance computing and embedded computing