## Slide 1: Trends in the Infrastructure of Computing
CSCE 190: Computing in the Modern World
Dr. Jason D. Bakos

## Slide 2: My Questions
How do computer processors work?
Why do computer processors get faster over time?
  How much faster do they get?
What makes one processor faster than another?
  What type of tradeoffs are involved in processor design?
  Why is my cell phone so much slower than my laptop?
What is the relationship between processor performance and how programs are written?
  Is this relationship dependent on the processor?

## Slide 3: Talk Outline
Quick introduction to how computer processors work
The role of computer architects
CPU design philosophy and survey of state-of-the art CPU technology
Coprocessor design philosophy and survey of state-of-art coprocessor technology
Reconfigurable computing
Heterogeneous computing
Brief overview of my research

## Slide 4: Semiconductors
Silicon is a group IV element
Forms covalent bonds with four neighbor atoms (3D cubic crystal lattice)
Si is a poor conductor, but conduction characteristics may be altered
Add impurities/dopants replaces silicon atom in lattice
  Adds two different types of charge carriers
Spacing = .543 nm

## Slide 5: MOSFETs
Metal-poly-Oxide-Semiconductor structures built onto substrate
  Diffusion: Inject dopants into substrate
  Oxidation: Form layer of SiO2 (glass)
  Deposition and etching: Add aluminum/copper wires
Cut away side view

## Slide 6: Layout
3-input NAND

## Slide 7: Logic Gates
inv
NAND2
NOR2

## Slide 8: Logic Synthesis
Behavior:
  S = A + B
  Assume A is 2 bits, B is 2 bits, C is 3 bits
A | B | C
00 (0) | 00 (0) | 000 (0)
00 (0) | 01 (1) | 001 (1)
00 (0) | 10 (2) | 010 (2)
00 (0) | 11 (3) | 011 (3)
01 (1) | 00 (0) | 001 (1)
01 (1) | 01 (1) | 010 (2)
01 (1) | 10 (2) | 011 (3)
01 (1) | 11 (3) | 100 (4)
10 (2) | 00 (0) | 010 (2)
10 (2) | 01 (1) | 011 (3)
10 (2) | 10 (2) | 100 (4)
10 (2) | 11 (3) | 101 (5)
11 (3) | 00 (0) | 011 (3)
11 (3) | 01 (1) | 100 (4)
11 (3) | 10 (2) | 101 (5)
11 (3) | 11 (3) | 110 (6)

## Slide 9: Microarchitecture

## Slide 10: Synthesized and P&R’ed MIPS Architecture

## Slide 11: Si Wafer

## Slide 12: Feature Size
Shrink minimum feature size…
  Smaller L decreases carrier time and increases current
  Therefore, W may also be reduced for fixed current
  Cg, Cs, and Cd are reduced
  Transistor switches faster (~linear relationship)

## Slide 13: Minimum Feature Size
Year | Processor | Performance | Transistor Size | Transistors
1982 | i286 | 6 - 25 MHz | 1.5 mm | ~134,000
1986 | i386 | 16 – 40 MHz | 1 mm | ~270,000
1989 | i486 | 16 - 133 MHz | .8 mm | ~1 million
1993 | Pentium | 60 - 300 MHz | .6 mm | ~3 million
1995 | Pentium Pro | 150 - 200 MHz | .5 mm | ~4 million
1997 | Pentium II | 233 - 450 MHz | .35 mm | ~5 million
1999 | Pentium III | 450 – 1400 MHz | .25 mm | ~10 million
2000 | Pentium 4 | 1.3 – 3.8 GHz | .18 mm | ~50 million
2005 | Pentium D | 2 threads/package | .09 mm | ~200 million
2006 | Core 2 | 2 threads/die | .065 mm | ~300 million
2008 | “Nehalem” | 8 threads/die | .045 mm | ~800 million
2009 | “Westmere” | 8 threads/die | .045 mm | ~1 billion
2011 | “Sandy Bridge” | 12 threads/die | .032 mm | ~1.2 billion
2012 | “Ivy Bridge” | 16 threads/die | .022 mm | ~1.4 billion
Year | Processor | Speed | Transistor Size | Transistors
2008 | NVIDIA Tesla (GT200) | 240 threads/die | .065 mm | 1.4 billion
2010 | NVIDIA Fermi (GF110) | 512 threads/die | .040 mm | 3.0 billion
2012 | NVNDIA Kepler (GK104) | 1536 threads/die | .028 mm | 3.5 billion

## Slide 14: The Role of Computer Architects
Given a blank slate (silicon substrate)
Budget: 2 billion transistors:
  Transistors  Area
2 cm
2 cm
Choose your components:
adder
multiplier
Component | Cost
Control Logic and Cache | 
Cache | 50K transistors/1KB + 10K transistors/port
Out-of-order instruction scheduler and dispatch | 200K transistors/core
Speculative execution | 400K transistors/core
Branch predictor | 200K transistors/core
Functional Units | 
Integer and load/store units | 100K transistors/unit/core
Floating-point unit | 1M transistors/unit/core
Vector/SIMD floating-point unit | 100M transistors/64b width/unit/core

## Slide 15: The Role of Computer Architects
Problem:
  Cost of fabricating one chip: Hundreds of millions of dollars
  Additional cost of fabricating hundreds of thousands of copies of same chip: FREE
Strategy for staying in business:
  Sell LOTS of chips
How to sell many chips:
  Make sure it works well for a wide range of applications (e.g. CPUs)
    Maximize performance of each thread, target small number of threads
  Works well for one application, but has a large market (e.g. GPUs, DSPs, smart phone processors, controllers for manufacturing)

## Slide 16: CPU Design Philosophy
Processors consist of three main componets:
  Control logic
  Cache
  Functional units
Premise:
  Most code (non scientific) isn’t written to take advantage of multiple cores
  Devote real estate budget to maximizing performance of each thread
    Control logic: reorders operations within a thread, speculatively execution
    Cache: reduces memory delays for different access patterns
CPUs do achieve higher performance when code is written to be multi-threaded
  But CPUs quickly run out of functional units

## Slide 17: CPU Design
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Control
L1 cache
L2 cache
Control
L1 cache
L2 cache
L3 cache
CPU
Core 1
Core 2
FOR i = 1 to 1000
C[i] = A[i] + B[i]
Copy part of A onto CPU
Copy part of B onto CPU
ADD
ADD
ADD
ADD
Copy part of C into Mem
time
Copy part of A onto CPU
Copy part of B onto CPU
ADD
ADD
ADD
ADD
Copy part of C into Mem
…
Thread 1
Thread 2

## Slide 18: Intel Sandy Bridge Architecture
Four cores, each core has 256-bit SIMD unit
Integrated GPU (IGU) with 12 execution units

## Slide 19: AMD Bulldozer Architecture
Next generation AMD architecture
Designed from scratch
Four cores, each core:
  Executes 2 threads with dedicated logic
  Contains two 128-bit FP multiply-add units
Decoupled L3 caches

## Slide 20: Graphical Processor Units (GPUs)
Basic idea:
  Originally designed for 3D graphics rendering
  Success in gaming market
  Devote real estate to computational resources
    As opposed to control and caches to make naïve and general-purpose code run fast
  Achieves very high performance but:
    Extremely difficult to program
      Program must be split into 1000s of threads
    Only works well for specific types of programs
    Lacks functionality to manage computer system resources
  Now widely used for High Performance Computing (HPC)

## Slide 21: Co-Processor (GPU) Design
ALU
ALU
ALU
ALU
cache
GPU
Core 1
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
Core 2
Core 3
Core 4
Core 5
Core 6
Core 7
Core 8
FOR i = 1 to 1000
C[i] = A[i] + B[i]
threads
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread

## Slide 22: NVIDIA GPU Architecture
Hundreds of simple processor cores
Core design:
  Executes each individual thread very slowly
  Each thread can only perform one operation at a time
  No operating system support
  Able to execute 32 threads
  Has 8 cores

## Slide 23: IBM Cell/B.E. Architecture
1 PPE, 8 SPEs
Programmer must manually manage 256K memory and threads invocation on each SPE
Each SPE includes a vector unit like the one on current Intel processors
  128 bits wide (4 ops)

## Slide 24: Intel Phi Coprocessor
PCIe coprocessor card
Used like a GPU
“Many Integrated Core”
  32 x86 cores, 128 threads
  512 bit SIMD units
  Coherent cache among cores
  2 GB onboard memory
  Uses Intel ISA

## Slide 25: Texas Instruments C66x Architecture
Originally designed for signal processing
8 decoupled cores
  No shared cache
Can do floating-point or fixed-point
  Can do fixed-point much faster
Possible coprocessor for HPC
  Less watts per FLOP

## Slide 26: ARM Cortex-A15 Architecture
Originally designed for embedded (cell phone) computing
Out-of-order superscalar pipelines
4 cores per cluster, up to 2 clusters per chip
Possible coprocessor for HPC?
  LOW POWER
    FLOPS/watt

## Slide 27: Field Programmable Gate Arrays
FPGAs are blank slates that can be electronically reconfigured
Allows for totally customized architectures
Drawbacks:
  More difficult to program than GPUs
  10X less logic density and clock speed

## Slide 28: Programming FPGAs

## Slide 29: Heterogeneous Computing
initialization
0.5% of run time
“hot” loop
99% of run time
clean up
0.5% of run time
49% of code
49% of code
2% of code
co-processor
Kernel speedup | Application speedup | Execution time
50 | 34 | 5.0 hours
100 | 50 | 3.3 hours
200 | 67 | 2.5 hours
500 | 83 | 2.0 hours
1000 | 91 | 1.8 hours
Combine CPUs and coprocs
Example:
  Application requires a week of CPU time
  Offload computation consumes 99% of execution time

## Slide 30: Heterogeneous Computing
CPU
X58
Host Memory
Co-processor
QPI
PCIe
On board
Memory
add-in card
host
General purpose CPU + special-purpose processors in one system
Use coprocessors to execute code that they can execute fast!
  Allow coprocessor to have its own high speed memory
25 GB/s
25 GB/s
8 GB/s (x16)
150 GB/s
Possible bottleneck!

## Slide 31: Heterogeneous Computing with FPGAs
Annapolis Micro Systems
WILDSTAR 2 PRO
GiDEL PROCSTAR III

## Slide 32: Heterogeneous Computing with FPGAs
Convey HC-1

## Slide 33: AMD Fusion Architecture
Integrate GPU-type coprocessor onto CPU
  Put a small RADEON GPU onto the CPU
Allows to accelerate smaller programs than PCIe-connected coprocessor
Targeted for embedded but AMD hopes to scale to servers

## Slide 34: My Research
Developed custom FPGA coprocessor architectures for:
  Computational biology
  Sparse linear algebra
  Data mining
Written GPU optimized implementations for:
  Computational biology
  Logic synthesis
  Data mining
  General purpose graph traversals
Generally achieve 50X – 100X speedup over general-purpose CPUs

## Slide 35: Current Research Goals
Develop high level synthesis (compilers) for specific types of FPGA-based computers
  Based on:
    Custom pipeline-based architectures
    Multiprocessor soft-core systems on reconfigurable chips (MPSoC)
Develop code tuning tools for GPU code based on runtime profiling analysis