## Slide 1: Heterogeneous Computing at USC Dept. of Computer Science and Engineering University of South Carolina
Dr. Jason D. Bakos
Assistant Professor
Heterogeneous and Reconfigurable Computing Lab (HeRC)
This material is based upon work supported by the National Science Foundation under Grant Nos. CCF-0844951 and CCF-0915608.

## Slide 2: Heterogeneous Computing
Subfield of computer architecture
Mix general-purpose CPUs with specialized processors
Becoming increasingly popular with high integration densities
GOALs:
  Explore the use of specialized processor designs that are designed with radically different designs than traditional CPUs
  Develop new programming models and methodologies for these processors

## Slide 3: Minimum Feature Size
Year | Processor | Speed | Transistor Size | Transistors
1982 | i286 | 6 - 25 MHz | 1.5 mm | ~134,000
1986 | i386 | 16 – 40 MHz | 1 mm | ~270,000
1989 | i486 | 16 - 133 MHz | .8 mm | ~1 million
1993 | Pentium | 60 - 300 MHz | .6 mm | ~3 million
1995 | Pentium Pro | 150 - 200 MHz | .5 mm | ~4 million
1997 | Pentium II | 233 - 450 MHz | .35 mm | ~5 million
1999 | Pentium III | 450 – 1400 MHz | .25 mm | ~10 million
2000 | Pentium 4 | 1.3 – 3.8 GHz | .18 mm | ~50 million
2005 | Pentium D | 2 threads/package | .09 mm | ~200 million
2006 | Core 2 | 2 threads/die | .065 mm | ~300 million
2008 | Core i7 “Nehalem” | 8 threads/die | .045 mm | ~800 million
2011 | “Sandy Bridge” | 16 threads/die | .032 mm | ~1.2 billion
Year | Processor | Speed | Transistor Size | Transistors
2008 | NVIDIA Tesla | 240 threads/die | .065 mm | 1.4 billion
2010 | NVIDIA Fermi | 512 threads/die | .040 mm | 3 billion

## Slide 4: CPU Design
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Control
L1 cache
L2 cache
Control
L1 cache
L2 cache
L3 cache
CPU
Core 1
Core 2
FOR i = 1 to 1000
C[i] = A[i] + B[i]
Copy part of A onto CPU
Copy part of B onto CPU
ADD
ADD
ADD
ADD
Copy part of C into Mem
time
Copy part of A onto CPU
Copy part of B onto CPU
ADD
ADD
ADD
ADD
Copy part of C into Mem
…

## Slide 5: Co-Processor Design
ALU
ALU
ALU
ALU
cache
GPU
Core 1
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
Core 2
Core 3
Core 4
Core 5
Core 6
Core 7
Core 8
FOR i = 1 to 1000
C[i] = A[i] + B[i]

## Slide 6: Heterogeneous Computing
CPU
X58
Host Memory
Co-processor
QPI
PCIe
On board
Memory
add-in card
host
General purpose CPU + special-purpose processors in one system
~25 GB/s
~25 GB/s
~8 GB/s (x16)
?????
~150 GB/s for GeForce 260
System I/O controller

## Slide 7: Heterogeneous Computing
initialization
0.5% of run time
“hot” loop
99% of run time
clean up
0.5% of run time
49% of code
49% of code
2% of code
co-processor
Kernel speedup | Application speedup | Execution time
50 | 34 | 5.0 hours
100 | 50 | 3.3 hours
200 | 67 | 2.5 hours
500 | 83 | 2.0 hours
1000 | 91 | 1.8 hours
Combine CPUs and coprocs
Example:
  Application requires a week of CPU time
  Offload computation consumes 99% of execution time

## Slide 8: NVIDIA GPU Architecture
Hundreds of simple processor cores
Core design:
  Only one instruction from each thread active in the pipeline at a time
  In-order execution
  No branch prediction
  No speculative execution
  No support for context switches
  No system support (syscalls, etc.)
  Small, simple caches
  Programmer-managed on-chip scratch memory

## Slide 9: Programming GPUs
HOST (CPU) code:
dim3 grid,block;
grid.x=((VECTOR_SIZE/512) + (VECTOR_SIZE%512?1:0));
block.x=512;
cudaMemcpy(a_device,a,VECTOR_SIZE * sizeof(double),cudaMemcpyHostToDevice);
cudaMemcpy(b_device,b,VECTOR_SIZE * sizeof(double),cudaMemcpyHostToDevice);
vector_add_device<<<grid,block>>>(a_device,b_device,c_device);
cudaMemcpy(c_gpu,c_device,VECTOR_SIZE * sizeof(double),cudaMemcpyDeviceToHost);
GPU code:
__global__ void vector_add_device (double *a,double *b,double *c) {
__shared__ double a_s,b_s,c_s;
a_s=a[blockIdx.x*blockDim.x+threadIdx.x];
b_s=b[blockIdx.x*blockDim.x+threadIdx.x];
c_s=a_s+b_s;
c[blockIdx.x*blockDim.x+threadIdx.x]=c_s;
}

## Slide 10: IBM Cell/B.E. Architecture
1 PPE, 8 SPEs
Programmer must manually manage 256K memory and threads invocation on each SPE
Each SPE includes a vector unit like the one on current Intel processors
  128 bits wide

## Slide 11: High-Performance Reconfigurable Computing
Heterogeneous computing with reconfigurable logic, i.e. FPGAs

## Slide 12: Field Programmable Gate Arrays

## Slide 13: Programming FPGAs

## Slide 14: Heterogeneous Computing with FPGAs
Annapolis Micro Systems
WILDSTAR 2 PRO
GiDEL PROCSTAR III

## Slide 15: Heterogeneous Computing with FPGAs
Convey HC-1

## Slide 16: Heterogeneous Computing with GPUs
NVIDIA Tesla S1070

## Slide 17: Heterogeneous Computing now Mainstream: IBM Roadrunner
Los Alamos, fastest computer in the world in 2008 (still in Top 10)
6,480 AMD Opteron (dual core) CPUs
12,960 PowerXCell 8i GPUs
Each blade contains 2 Operons and 4 Cells
296 racks
First ever petaflop machine (2008)
1.71 petaflops peak (1.7 billion million fp operations per second)
2.35 MW (not including cooling)
  Lake Murray hydroelectric plant produces ~150 MW (peak)
  Lake Murray coal plant (McMeekin Station) produces ~300 MW (peak)
  Catawba Nuclear Station near Rock Hill produces 2258 MW

## Slide 18: Research Problems
What is the best way to design coprocessors? How can we make them faster and easier to program?
  Approach: Perform design-space exploration using simulations, mostly in the hands of big companies
What is the best way to design heterogeneous machines? How do we interconnect the CPU and coprocessors?
  Approach: PCI-express was the enabler of modern heterogeneous systems and QPI and Hypertransport may make things even easier in the future
  However, scalability is still a major problem, right now people use hierarchical systems
How well do certain types of (scientific) programs run on heterogeneous machines? What benefit should we expect?
  Approach: Perform “by hand” acceleration of specific applications and report results
How do you modify an arbitrary program to run on a heterogeneous machine?
  Approach: Same as above, but use these experiences to develop new development tools and methodologies that are general-purpose

## Slide 19: Our Group: HeRC
Applications work
  Computational phylogenetics (FPGA/GPU)
    GRAPPA and MrBayes
  Sparse linear algebra (FPGA/GPU)
    Matrix-vector multiply, double-precision accumulators
  Data mining (FPGA/GPU)
  Logic minimization (GPU)
System architecture
  Multi-FPGA interconnects
Tools
  Automatic partitioning (PATHS)
  Micro-architectural simulation for code tuning
Chart: 
| applications | system arch | tools
 | 0.7 | 0.05 | 0.25

## Slide 20: Application: Phylogenies
genus Drosophila

## Slide 21: Application: Phylogenies
g1
g2
g5
g4
g6
g3
g5
g4
g1
g3
g2
g5
g6
g5
g5
g2
g1
g6
g3
g4
Unrooted binary tree
n leaf vertices
n - 2 internal vertices (degree 3)
Tree configurations =
  (2n - 5) * (2n - 7) * (2n - 9) * … * 3
200 trillion trees for 16 leaves

## Slide 22: Our Applications Work
FPGA-based co-processors for computational biology
Tiffany M. Mintz, Jason D. Bakos, "A Cluster-on-a-Chip Architecture for High-Throughput Phylogeny Search," IEEE Trans. on Parallel and Distributed Systems, in press.
Stephanie Zierke, Jason D. Bakos, "FPGA Acceleration of Bayesian Phylogenetic Inference," BMC Bioinformatics, in press.
Jason D. Bakos, Panormitis E. Elenis, "A Special-Purpose Architecture for Solving the Breakpoint Median Problem," IEEE Transactions on Very Large Scale Integration (VLSI) Systems, Vol. 16, No. 12, Dec. 2008.
Jason D. Bakos, Panormitis E. Elenis, Jijun Tang, "FPGA Acceleration of Phylogeny Reconstruction for Whole Genome Data," 7th IEEE International Symposium on Bioinformatics & Bioengineering (BIBE'07), Boston, MA, Oct. 14-17, 2007.
Jason D. Bakos, “FPGA Acceleration of Gene Rearrangement Analysis,” 15th Annual IEEE International Symposium on Field-Programmable Custom Computing Machines (FCCM'07), April 23-25, 2007.
1000X speedup!
10X speedup!

## Slide 23: Our Applications Work
FPGA-based co-processors for linear algebra
Krishna.K. Nagar, Jason D. Bakos, "A High-Performance Double Precision Accumulator," IEEE International Conference on Field-Programmable Technology (IC-FPT'09), Dec. 9-11, 2009.
Yan Zhang, Yasser Shalabi, Rishabh Jain, Krishna K. Nagar, Jason D. Bakos, "FPGA vs. GPU for Sparse Matrix Vector Multiply," IEEE International Conference on Field-Programmable Technology (IC-FPT'09), Dec. 9-11, 2009.
Krishna K. Nagar, Yan Zhang, Jason D. Bakos, "An Integrated Reduction Technique for a Double Precision Accumulator," Proc. Third International Workshop on High-Performance Reconfigurable Computing Technology and Applications (HPRCTA'09), held in conjunction with Supercomputing 2009 (SC'09), Nov. 15, 2009.
Jason D. Bakos, Krishna K. Nagar, "Exploiting Matrix Symmetry to Improve FPGA-Accelerated Conjugate Gradient," 17th Annual IEEE International Symposium on Field Programmable Custom Computing Machines (FCCM'09), April 5-8, 2009.

## Slide 24: Our Applications Work
FPGA-based co-processors for linear algebra
Krishna.K. Nagar, Jason D. Bakos, "A High-Performance Double Precision Accumulator," IEEE International Conference on Field-Programmable Technology (IC-FPT'09), Dec. 9-11, 2009.
Yan Zhang, Yasser Shalabi, Rishabh Jain, Krishna K. Nagar, Jason D. Bakos, "FPGA vs. GPU for Sparse Matrix Vector Multiply," IEEE International Conference on Field-Programmable Technology (IC-FPT'09), Dec. 9-11, 2009.
Krishna K. Nagar, Yan Zhang, Jason D. Bakos, "An Integrated Reduction Technique for a Double Precision Accumulator," Proc. Third International Workshop on High-Performance Reconfigurable Computing Technology and Applications (HPRCTA'09), held in conjunction with Supercomputing 2009 (SC'09), Nov. 15, 2009.
Jason D. Bakos, Krishna K. Nagar, "Exploiting Matrix Symmetry to Improve FPGA-Accelerated Conjugate Gradient," 17th Annual IEEE International Symposium on Field Programmable Custom Computing Machines (FCCM'09), April 5-8, 2009.

## Slide 25: Streaming Double Precision Accumulation
FPGAs allow data to be “streamed” into a computational pipeline
Many kernels targeted for acceleration include
  Such as: dot product, used for MVM: kernel for many methods
For large datasets, values delivered serially to an accumulator
  Reduction operation
A,
set 1
Σ
B,
set 1
C,
set 1
D,
set 2
E,
set 2
F,
set 2
G,
set 3
A+B+C,
set 1
D+E+F,
set 2
H,
set 3
I,
set 3
G+H+I,
set 3

## Slide 26: The Reduction Problem
+
Mem
Mem
Control
Partial sums
Basic Accumulator Architecture
Adder Pipeline
Required Design
Reduction Ckt
Feedback Loop

## Slide 27: Sparse Matrix-Vector Multiply
A
0
0
0
B
0
0
0
0
C
0
D
E
0
0
0
F
G
H
0
0
0
0
0
0
0
I
0
J
0
0
0
0
K
0
0
val
col
ptr
A
B
C
D
E
F
G
H
I
J
K
0
4
3
5
0
4
5
0
2
4
3
0
2
4
7
8
10
11
0
1
2
3
4
5
6
7
8
9
10
(A,0) (B,4) (0,0) (C,3) (D,4) (0,0)…
Group vol/col
Zero-terminate

## Slide 28: New SpMV Architecture
Delete tree, replicate accumulator, schedule matrix data:
val0,0 | col0,0 | val1,0 | col1,0 | val2,0 | col2,0 | val3,0 | col3,0 | val4,0 | col4,0
val0,1 | col0,1 | val1,1 | col1,1 | val2,1 | col2,1 | val3,1 | col3,1 | val4,1 | col4,1
val0,2 | col0,2 | val1,2 | col1,2 | val2,2 | col2,2 | val3,2 | col3,2 | val4,2 | col4,2
val0,3 | col0,3 | val1,3 | col1,3 | val2,3 | col2,3 | val3,3 | col3,3 | val4,3 | col4,3
val0,4 | col0,4 | val1,4 | col1,4 | val2,4 | col2,4 | val3,4 | col3,4 | val4,4 | col4,4
val0,5 | col0,5 | val1,5 | col1,5 | val2,5 | col2,5 | val3,5 | col3,5 | val4,5 | col4,5
val0,6 | col0,6 | 0.0 | 0.0 | val2,6 | col2,6 | val3,6 | col3,6 | val4,6 | col4,6
val0,7 | col0,7 | 0.0 | 5 | val2,7 | col2,7 | val3,7 | col3,7 | val4,7 | col4,7
val0,8 | col0,8 | val5,0 | col5,0 | val2,8 | col2,8 | val3,8 | col3,8 | val4,8 | col4,8
400 bits

## Slide 29: Performance Comparison
If FPGA Memory bandwidth scaled by adding multipliers/ accumulators to match GPU Memory Bandwidth for each matrix separately
GPU Mem. BW (GB/s) | FPGA Mem BW (GB/s)
58.00 | 51.0 GB/s (x6)
57.03 | 51.0 GB/s (x6)
52.58 | 51.0 GB/s (x6)
49.16 | 42.5 GB/s (x5)
40.23 | 34 GB/s (x4)
26.64 | 25.5 GB/s (x3)
25.68 | 25.5 GB/s (x3)
27.66 | 25.5 GB/s (x3)
27.08 | 25.5 GB/s (x3)
Chart: 
| TSOPF_RS_b162_c3 | E40r1000 | Simon/olafu | Garon/garon2 | Mallya/lhr11c | Hollinger/mark3jac020sc | Bai/dw8192 | YCheng/psse1 | GHS_indef/ncvxqp1
GPU GFLOPS | 10.08 | 8.76 | 8.52 | 7.18 | 5.1 | 1.58 | 1.28 | 1.24 | 0.98
FPGA GFLOPS | 9.59 | 9.87 | 10.03 | 8.18 | 5.94 | 3.28 | 3.24 | 2.54 | 3.38

## Slide 30: Sequence Alignment
DNA/protein sequence, e.g.
  TGAGCTGTAGTGTTGGTACCC => TGACCGGTTTGGCCC
Goal: align the two sequences against substitutions and deletions:
  TGAGCTGTAGTGTTGGTACCC
  TGAGCTGT----TTGGTACCC
Used for sequence comparison and database search

## Slide 31: GPU and FPGA Acceleration of Data Mining
Minimum support=2
<BCE>
<ABC>, <ABE>, <ACE>, <BCE>

## Slide 32: Our Applications Work
GPU Acceleration of Two Level Logic Minimization
1. Ibrahim Savran, Jason D. Bakos, "GPU Acceleration of Near-Minimal Logic Minimization," 2010 Symposium on Application Accelerators in High Performance Computing (SAAHPC'10), July 13-15, 2010.
A | B | C | D | out
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
anything else |  |  |  | X
A’B’D’
A’BC
(ACD)’
(A’BC’D)’
A’B’CD
A’B’C’D
A’B’
A’B’CD
A’B’CD’
A’C

## Slide 33: Our Projects
Multi-FPGA System Architectures
Jason D. Bakos, Charles L. Cathey, E. Allen Michalski, "Predictive Load Balancing for Interconnected FPGAs," 16th International Conference on Field Programmable Logic and Applications (FPL'06), Madrid, Spain, August 28-30, 2006.
Charles L. Cathey, Jason D. Bakos, Duncan A. Buell, "A Reconfigurable Distributed Computing Fabric Exploiting Multilevel Parallelism," 14th Annual IEEE International Symposium on Field-Programmable Custom Computing Machines (FCCM'06), April 24-26, 2006.
GPU Simulation
Patrick A. Moran, Jason D. Bakos, "A PTX Simulator for Performance Tuning CUDA Code," IEEE Trans. on Parallel and Distributed Systems, submitted.

## Slide 34: PATHS: Task Partitioning for Heterogeneous Computing

## Slide 35: High-Level Synthesis
Input bandwidth-constrained high-level synthesis
Example: 16-input expression:
out = (AA1 * A1 + AC1 * C1 + AG1 * G1 + AT1 * T1) *
(AG2 * A2 + AC2 * C2 + AG2 * G2 + AT2 * T2)

## Slide 36: Contact Information
Jason D. Bakos
  Office: 3A52
  E-mail: jbakos@sc.edu
  http://www.cse.sc.edu/~jbakos
Heterogeneous and Reconfigurable Computing (HeRC) Lab:
  Lab: 3D15
  http://herc.cse.sc.edu

## Slide 37: Acknowledgement
Heterogeneous and Reconfigurable Computing Group
http://herc.cse.sc.edu
Zheming Jin
Tiffany Mintz
Krishna Nagar
Jason Bakos
Yan Zhang