## Slide 1: Lightweight Hierarchical Error Control Codes for Multi-Bit Differential Channels
Jason D. Bakos
Ph.D. Committee:
Donald M. Chiarulli
Steven P. Levitan
Bruce R. Childers
Patchrawat Uthaisombut

## Slide 2: Introduction
New class of error control codes
  “Lightweight Hierarchical Error Control Codes”
  Applicable to system-level interconnect
  Operates over new high-performance system-level interconnect technology
    “Multi-Bit Differential Signaling (MBDS)”
  Uses inherent properties of MBDS to achieve error control while requiring minimal data and logic overhead

## Slide 3: System-Level Interconnect
Network-on-chip
Printed circuit boards
Multi-Chip Modules
Backplanes
Peripherals
System-level interconnect
  Short-haul
  High-speed

## Slide 4: Challenges for System-Level Interconnect
Signal integrity
  Capacitance, inductance
  Noise, crosstalk
  Synchronization/jitter
Area
  I/O pads precious
  Driver size
Packaged chip
Packaged chip
Source: Intel Corporation

## Slide 5: Error Control Codes
Error control codes used to increase signal integrity over noisy channels
Examples:
  Cellular networks, deep-space signaling, digital TV transmission, hard/optical disks
  Low-speed channels
ECC codes require information overhead
  Acceptable for low-speed channels
  Minimize by applying code over large blocks of data
  Example:
    187 bytes for HDTV

## Slide 6: Error Control Codes
ECC over large blocks requires complex decoding
  Memory, latency
  Encoding/decoding logic complexity
Encoding/decoding performed using software or dedicated ASICs
  Performed at Mb/s-speeds
Traditional ECC codes not practical for system-level interconnect
  Encode/decode in small area
  High-throughput (core speed)
Need new class of ECC code for system-level interconnect
  Small block size
  Low overhead

## Slide 7: Talk Outline
Multi-Bit Differential Signaling (MBDS)
  “N choose M” data encoding
Lightweight Hierarchical Error Control Codes (LHECC)
Encoder/decoder implementation
Experimental verification
  Link modeling
  Noise modeling
Experimental results
Conclusion

## Slide 8: Multi-Bit Differential Signaling (MBDS)
Differential (LVDS) channels
Current-mode drivers
Data encoded as
  {01} or {10}
Advantages
  Low switching noise
  Large GDP
  Common-mode noise rejection
  EM coupled transmission lines
  Low noise => low voltage swing
Disadvantages
  Wasteful in I/O pads
Multi-Bit Differential (MBDS) channel
Scale up LVDS driver
Data encoded with fixed number of ones
“N-choose-M (nCm)” symbols
  {0011}, {0101}, {0110}, {1001}, {1010}, {1100}
Advantages
  Same transmission characteristics as differential
  Higher information capacity

## Slide 9: MBDS / “n choose m (nCm)” Encoding
Symbol set size
Effective bits
EXAMPLE
6-wire MBDS channel
20 symbols
effective bits = 4
equivalent to 8-wire differential channel
25% fewer pads (8 versus 6)
25% less power (4 1-bits on versus 3)

## Slide 10: nCm Encoding: Unused Symbol Space
Each nCm symbol set has unmapped symbols
0011
0101
0110
1001
1010
1100
00
01
10
11
?
?
4c2 symbols => binary value
4c2
4c2
36 combinations
5 bits
2 bits
2 bits
6 sym
6 sym
Solution #1
  Use multiple MBDS channels in parallel
Solution #2
  Exclude symbols for purposes of ECC

## Slide 11: nCm Encoding: Inherent Error Detection
Most types of symbol errors can be detected at receiver
0011
1011
0111
0001
0010
1101
1110
1000
0100
1 error
3 errors
Odd-number of bit errors
Even-number of bit errors
0011
1111
1001
1010
0101
0110
0000
2 errors

## Slide 12: nCm Encoding: Inherent Error Detection
Chan | P(detect 2-bit error) | P(detect 4-bit error) | P(detect 6-bit error) | P(detect 8-bit error)
4c2 | 33% |  |  | 
6c3 | 40% | 40% |  | 
8c4 | 43% | 49% | 43% | 
10c5 | 56% | 48% | 48% | 56%

## Slide 13: Talk Outline
Multi-Bit Differential Signaling (MBDS)
  “N choose M” data encoding
Lightweight Hierarchical Error Control Codes (LHECC)
Encoder/decoder implementation
Experimental verification
  Link modeling
  Noise modeling
Experimental results
Conclusion

## Slide 14: Hierarchical Encoding
Symbolic ECC block
Code word over parallel MBDS channels
start with raw binary data
Encode portion of data, set rules for nCm symbol selection
Encode remainder of data using nCm symbols
high-level code
low-level code
LHECC relies on a hierarchical approach to encoding
s-data
c-data
Binary source data

## Slide 15: Low-Level Code
nCm symbol sets have Hamming distance (d) = 2
Correctable bits = floor((d-1)/2)
Set new distance by partitioning into equal-size subsets
  s subsets, c symbols/subset
0011
0101
1010
1001
0110
1100
Example:
4c2, distance=4
Subsets:
  0 => {0011, 1100}
  1 => {0101, 1010}
  2 => {0110, 1001}
If subset is known, bit errors may be corrected
  Example: 0111, subset=2
  Correct to 0110
Performed off-line

## Slide 16: Partitioning Operation
Perform search over space of assignments
Must know: distance, # subsets (s), and symbols/subset (c)
Minimize s while maximizing c
000111
001011
001101
001110
010011
010101
010110
011001
011010
011100
100011
100101
100110
101001
101010
101100
110001
110010
110100
111000
Example: 6c3, 4/4, distance=4
subset 0:
subset 1:
subset 2:
subset 3:
000111
011100
101010
110001
001011
010110
100101
111000
001101
011010
100011
110100
001110
010101
101001
110010
Result:
Each nCm symbol becomes associated with an s-data component and a c-data component
Example: 100101
s-data: 1
c-data: 2
0:
1:
2:
3:
0:
1:
2:
3:
0:
1:
2:
3:
0:
1:
2:
3:

## Slide 17: High-Level Code: Linear Block Codes
k data symbols
n-k parity symbols
block size=n
Can correct:
erasures
errors
Checksum
  Requires 1 parity symbol
  Can correct 1 erasure
Near-MDS code
  Corrects erasures:
    Number of parity symbols - 1
  Corrects errors:
    (Number of parity symbols – 1) / 2
  Restrictions:
    Symbol base must be prime or power of a prime
    If symbol base = pm, max block size = pm+1 - 1
MDS code (Reed-Solomon)
  Can correct erasures within block:
    Number of parity symbols
  Can correct errors within block:
    Number of parity symbols / 2
  Restrictions:
    Symbol base must be prime or power of a prime
    Max block size = symbol base + 1

## Slide 18: Encoding LHECC
0101001001
0010010100
(s-data)
(c-data)
b bits
01010010010010010100
Parity symbols
Data symbols
base conv. 2->s
Data as nCm symbols
Parity as nCm symbols
base conv. 2->c

## Slide 19: Code Rate and Overhead
LHECC codes are defined as (nCm,n,k,dh,s,c,dl) codes
High-level code: k*log2(s) bits
Low-level code: n*log2(c) bits
Advantages over traditional block ECC:
  Requires less number of parity symbols for correction
  Parity symbols carry data

## Slide 20: Example #1: Encoding
Assume 3 x 4c2 channels
  Low level
    s=3, c=2
  High level
    (3,2) checksum code
  s-data
    32 = 9 cw (3 bits)
  c-data
    23 = 8 cw (3 bits)
  6 bits / 12 wires
  rel=1.0, abs=0.5, oh=0
  Can correct one bit error within 1 symbol
Encode 111101…
2
1
1112 = 213
2
1
0
Compute checksum parity…
Encode 101…
2
1
0
1
0
1
bit
sub.
1001
0101
1100

## Slide 21: Example #1: Decoding
Assume bit error occurs…
0 – 1 = 2 (mod 3)
  Symbol in error must be 0110 or 1001
  dist(1101,0110) = 3, dist(1101,1001) = 1
  Corrected symbol is 1001
Decoder:
  If invalid code word is detected
    Determine subset
    Use minimum distance decoder
1001
0101
1100
1101
0101
1100
?
1
0
2
1
0
sub.
sym

## Slide 22: Example #2: Encoding
Assume 4 x 4c2 channels
  s=3, c=2
  (4,2) MDS code
  s-data
    32 = 9 symbols (3 bits)
  c-data
    24 = 16 symbols (4 bits)
  7 bits / 16 wires
  rel=7/8=.88, abs=.44, oh=1 bit
  Can correct one bit error in two symbols
Need MDS generator matrix for encoding
  G = [ Ik Ak x (n-k) ]
Need MDS parity-check matrix for decoding
  H = [ -AT In-k]

## Slide 23: Example #2: Encoding
Encode 1010...
1
1
2
0
1
0
1
0
bit
sub.
Encode 1001010…
1
1
100
1010
0101
1001
0011
2
0

## Slide 24: Example 2: Erasure Decoding
1010
0101
1001
0011
1110
0101
1001
0001
0 => {0011, 1100}
1 => {0101, 1010}
2 => {0110, 1001}
?
1
2
?
sub.
1
0
1010
0101
1001
0011
(recover s-data)
113 = 1002
dist(1110,0101)=3
dist(1110,1010)=1
dist(0001,0011)=1
dist(0001,1100)=3
(recover c-data)
grp.
1
1
2
0
bit
1
0
1
0
1
1
2
0
sub.

## Slide 25: Example 2: Error Decoding
1010
0101
1001
0011
0110
0101
1001
0011
2
1
2
0
sub.
0 => {0011, 1100}
1 => {0101, 1010}
2 => {0110, 1001}
1
1
2
0
sub.
dist(0110,0101)=2
dist(0110,1010)=2
Can’t correct nCm symbol without partitioning for more distance
no error

## Slide 26: Example 3: Multiple Bit Error Correction
4 x 6c3 channels
9 subsets, 2 sym/subset, distance=6
Assume (4,2,3) MDS code
rel=10/16=.63, abs=10/24=42%
010110
110010
100101
001011
6
2
8
1
sub.
010110
110010
101001
001011
6
2
6
1
sub.
dist(101001,011010)=4
dist(101001,100101)=2
corrected symbol is 100101

## Slide 27: LHECC Theory
LHECC is equivalent to binary code space over MBDS channels
Example: LHECC-encoded code word
  high-level distance=2
  low-level distance=4
  Assume inter-subset distance=2
s-data: 111, c-data: 110
0101
0101
0101
s-data: 111, c-data: 111
0101
0101
1010
Hamming displacement=4
s-data: 101, c-data: 110
0101
0011
1001
Hamming displacement=2
Hamming displacement=2

## Slide 28: Example Partitionings
symbol set | symbols | subsets (s) | symbols/subset (c) | distance | overhead/parity | relative overhead
4c2 | 6 | 3 | 2 | 4 | 1.5 | .79
6c3 | 20 | 10 | 2 | 6 | 3.3 | .83
6c3 | 20 | 4 | 4 | 4 | 2 | .50
8c4 | 70 | 10 | 7 | 4 | 3.3 | .55
8c4 | 70 | 35 | 2 | 8 | 5.1 | .85
8c4 | 70 | 7 | 9 | 4 | 2.8 | .47
8c4 | 70 | 8 | 8 | 4 | 3 | .50
10c5 | 252 | 8 | 16 | 4 | 3 | .43
10c5 | 252 | 32 | 6 | 6 | 5 | .71
12c6 | 924 | 8 | 64 | 4 | 3 | .33

## Slide 29: Talk Outline
Multi-Bit Differential Signaling (MBDS)
  “N choose M” data encoding
Lightweight Hierarchical Error Control Codes (LHECC)
Encoder/decoder implementation
Experimental verification
  Link modeling
  Noise modeling
Experimental results
Conclusion

## Slide 30: Encoder/Decoder Implementation
Responsible for binary-to-nCm conversion as well as error detection/correction
Encoders/decoders should be small
Should operate at core speed
  Hierarchical encoding/decoding lends itself to pipelined implementation
Synthesized using standard cell library
  Latch, inverter, 2/3-input NAND, 2/3-input NOR
Example interconnect organization:
receiver
binary
receiver
receiver
binary
encoder
driver
driver
driver
decoder

## Slide 31: 3x6c3 Encoder Implementation
s-data (4 bits)
c-data (6 bits)
checksum
checksum (2-bits)
pipeline reg (12 bits)
19 gates
5 gate delays
gen. cw
gen. cw
gen. cw
sa(2)
ca(2)
sb(2)
cb(2)
ss(2)
cs(2)
6c3 (a)
6c3 (b)
6c3 (s)
EACH:
63 gates
5 gate delays
pipeline reg (18 bits)
Implement a 3x6c3 code (1 bit error in 1 symbol)
s-data is 2*log2(4) = 4 bits
c-data is 3*log2(4) = 6 bits
Carries 10 bits over 18 wires
Relative code rate = 10 / (3*4) = 83.3%
Absolute code rate = 10 / 18 = 55.6%
Total:
208 gates, 30 latches
High-level code
Low-level code

## Slide 32: 3x6c3 Decoder Implementation
6c3
6c3
6c3
ea
sa(2)
eb
sb(2)
es
ss(2)
ca(2)
cb (2)
cs (2)
pipeline reg (18 bits)
resolver
resolver
resolver
pipeline reg (33 bits)
130x3 gates
7 gate delays
md_decoder stage 1
corr_s(2)
cw(6)
sa(2)
corr_s(2)
sb(2)
corr_s(2)
16 gates
3 gate delays
xora (6)
xorb (6)
xorc (6)
xord (6)
sa(2)
sb(2)
err flags(3)
c-data(6)
nofix
84 gates
6 gate delays
xora (6)
xorb (6)
xorc (6)
xord (6)
corr_c(2)
md_err
md_decoder stage 2
pipeline reg (17 bits)
sa(2)
sb(2)
c-data(6)
nofix
err flags(3)
118 gates
8 gate delays
c-data (6)
c_error(2)
corr_c(2)
cb(2)
corr_c(2)
cs(2)
corr_c(2)
ca(2)
s-data (4)
err flags(3)
nofix
cerror
6 gates
2 gate delays
md_err
24 gates
3 gate delays
blk_error detector
blk-corrector
err flags(3)
s-data (4)
cwb(6)
cws(6)
cwa(6)
nofix
corr_s(2)
cw(6)
c-data(6)
47 gates
7 gate delays
49 gates
7 gate delays
96 gates
6 gate delays
pipeline reg (22 bits)
Total:
830 gates,
128 latches
pipeline reg (38 bits)
Resolver
High-level code
Low-level code 1
Low-level code 2
Routing

## Slide 33: Encoder/Decoder Implementations
Itrct | Width | Correction capability | Encoder |  |  | Decoder |  |  | Max latency/stage
 |  |  | Gates | Latches | Stages | Gates | Latches | Stages | 
3x4c2 | 12 | 1 bit/1 sym | 100 | 28 | 3 | 328 | 66 | 5 | 7
4x4c2 | 16 | 1 bit/2 sym | 144 | 36 | 3 | 804 | 124 | 6 | 8
3x6c3 | 18 | 1 bit/1 sym | 208 | 30 | 2 | 830 | 128 | 6 | 8
3x8c4 | 24 | 1 bit/1 sym | 424 | 44 | 2 | 1246 | 234 | 6 | 8

## Slide 34: Talk Outline
Multi-Bit Differential Signaling (MBDS)
  “N choose M” data encoding
Lightweight Hierarchical Error Control Codes (LHECC)
Encoder/decoder implementation
Experimental verification
  Link modeling
  Noise modeling
Experimental results
Conclusion

## Slide 35: PCB Interconnect Model
CMOS code words in
CMOS code words out
Driver input
Receiver output
Input is sampled at midpoint
Outputs sampled at t(input) + latency
cwn
cwn+1
cwn-1
cwn
cwn+1
cwn-1
latency
Replicated for each channel forming the interconnect
Single MBDS channel

## Slide 36: Driver/Receiver Modeling
Bias input
4c2 input
4c2 output
MOSFET models from TSMC .18 um PDK
Bias current = 7.5 mA mean-abs current per leg
Driver circuit
Receiver circuit
source: Stefan Hirsch, Hans-Jörg Pfleiderer, “CMOS receiver circuits for high-speed data transmission according to LVDS-standard,” Proceedings of SPIE Vol. 5117 (2003).

## Slide 37: Package Modeling
solder bump model
wire bond model
solder bump model

## Slide 38: PCB Transmission Line Modeling
FR4 PCB material
Individual t-lines matched to 50 ohms
Width=16 mil, thickness=1.4 mil, distance=16 mil
Layer spacing based on commercial PCB process
Fully coupled transmission line models
Ground capacitance, serial inductance
Coupled with mutual capacitance, mutual inductance
4c2
6c3
8c4
Length=7.5”

## Slide 39: Noise Modeling
Goal: Capture link behavior in the presence of noise
Error sources from link model:
  Transistors: jitter, switching noise
  Transmission lines: frequency-dependant attenuation, crosstalk
Receivers discriminate signal to convert to digital
Input to receiver
Receiver output
1.8 GCW/s
2.2 GCW/s
2.6 GCW/s
3.0 GCW/s
3.4 GCW/s
3.8 GCW/s
4.2 GCW/s
4.6 GCW/s

## Slide 40: Supply Noise
Intel: Busy 1.5 V Pentium 4 processor:
  Stddev = 17-20 mV
Add independent Vdd noise to driver and receiver
To generate:
  Assume links operating at core switching frequency
  Generate white Gaussian noise
    Sampled at 20 GHz for 20 us
  Apply passband filter to noise, 200 MHz band centered on op. frequency
Source: private correspondence with Martin Saint-Laurent, Intel Corporation

## Slide 41: Fringe Capacitance in Driver
Fringe capacitance from circuit layouts and packaging add parasitic capacitance effects
  Where it hurts channel most (noise source)
  Adds additional crosstalk

## Slide 42: Experimental Verification
Goal: measure amount of improvement in channel performance from the addition of LHECC support to MBDS links
Setup 5 interconnects with various capacities and levels of error control
Simulate interconnects with analog simulator
  Test each link with a random sequence of 100,000 code words transmitted at several code word transmission rates
Measure error rates for each test at the output of receivers for links with and without LHECC support
Determine maximum transmission rate for code word error rate < 10-5

## Slide 43: Experimental Interconnects
Correct 1 symbol containing 1 bit error
Intercnt | width | capacity (no-ecc) | capacity (ecc) | rel. code rate
3x4c2 | 12 | 6/.50 | 6/.50 | 1.00
3x6c3 | 18 | 12/.67 | 10/.56 | .83
3x8c4 | 24 | 18/.75 | 15/.63 | .83
Correct 2 symbols containing 1 bit error
Intercnt | width | capacity (no-ecc) | capacity (ecc) | rel. code rate
4x4c2 | 16 | 8/.50 | 7/.44 | .88
Correct 2 symbols containing 2 bit errors or 1 symbol containing 2 bits where errors yield valid nCm symbol
Intercnt | width | capacity (no-ecc) | capacity (ecc) | rel. code rate
4x6c3 | 24 | 16/.67 | 10/.42 | . 63

## Slide 44: Talk Outline
Multi-Bit Differential Signaling (MBDS)
  “N choose M” data encoding
Lightweight Hierarchical Error Control Codes (LHECC)
Encoder/decoder implementation
Experimental verification
  Link modeling
  Noise modeling
Experimental results
Conclusion

## Slide 45: Experimental Results: Internal noise sources only (transistor noise, channel crosstalk)
Interconnect | max t-rate (no-ecc) | max t-rate (ecc) | relative increase | relative increase wrt code rate
3x4c2 | 3.4 GHz | 4.2 GHz | 24% | 24%
3x6c3 | 3.0 GHz | 4.0 GHz | 33% | 11%
3x8c4 | 2.8 GHz | 3.8 GHz | 36% | 13%

## Slide 46: Experimental Results: P4 supply noise characteristics added
Interconnect | max t-rate (no-ecc) | max t-rate (ecc) | relative increase | relative increase wrt code rate
3x4c2 | 3.2 GHz | 4.0 GHz | 25% | 25%
3x6c3 | 2.8 GHz | 3.8 GHz | 36% | 13%
3x8c4 | 2.6 GHz | 3.8 GHz | 46% | 22%

## Slide 47: Experimental Results: Crosstalk from fringe capacitance
Interconnect | max t-rate (no-ecc) | max t-rate (ecc) | relative increase | relative increase wrt code rate
3x4c2 | 2.8 GHz | 3.8 GHz | 36% | 36%
3x6c3 | 2.6 GHz | 3.6 GHz | 38% | 15%
3x8c4 | 2.2 GHz | 3.6 GHz | 64% | 36%

## Slide 48: Experimental Results (multi-symbol ECC)
Interconnect | max t-rate (no-ecc) | max t-rate (ecc) | relative increase | relative increase (code rate)
4x4c2 | 3.4 GHz | 4.4 GHz | 29% | 13%
4x6c3 | 2.6 GHz | 4.4 GHz | 69% | 6%
Internal noise sources only

## Slide 49: Experimental Results (multi-symbol ECC)
Interconnect | max t-rate (no-ecc) | max t-rate (ecc) | relative increase | relative increase (code rate)
4x4c2 | 3.0 GHz | 4.4 GHz | 47% | 28%
4x6c3 | 2.4 GHz | 4.2 GHz | 75% | 9%
Supply noise characteristics added

## Slide 50: Experimental Results (multi-symbol ECC)
Interconnect | max t-rate (no-ecc) | max t-rate (ecc) | relative increase | relative increase (code rate)
4x4c2 | 2.6 GHz | 3.8 GHz | 46% | 28%
4x6c3 | 2.2 GHz | 4.0 GHz | 82% | 14%
Crosstalk from fringe capacitance

## Slide 51: Talk Outline
Multi-Bit Differential Signaling (MBDS)
  “N choose M” data encoding
Lightweight Hierarchical Error Control Codes (LHECC)
Encoder/decoder implementation
Experimental verification
  Link modeling
  Noise modeling
Experimental results
Conclusion

## Slide 52: Conclusions and Future Work
Conclusions
  LHECC is effective at achieving low overhead error control
  LHECC encoders/decoders viable for system interconnect
    small, fast
  LHECC verified to increase noise immunity for MBDS interconnects
  Greatest benefit from single-symbol ECC
    Steepness of error rate curve for MBDS interconnects
Future Work
  Design and test fabricated LHECC interconnects