## Slide 1: Integrated Circuit Design and Fabrication
Dr. Jason D. Bakos

## Slide 2: Elements

## Slide 3: Semiconductors
forward bias
reverse bias
+ + +
+ + +
- - -
- - -
P-N junction
+
-
-
+
+ + +
+ + +
- - -
- - -

## Slide 4: MOSFETs
body/bulk
GROUND
NMOS
PMOS
channel
shorter length, faster transistor (dist. for electrons)
body/bulk
HIGH
positive voltage (Vdd)
negative voltage (rel. to body) (GND)
- - -
+ + +
+ + +
- - -
current
current

## Slide 5: Logic Gates
inv
NAND2
NOR2
A | Y
0 | 1
1 | 0
A | B | Y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 6: IC Fabrication
Inverter cross-section
field oxide

## Slide 7: Layout
3-input NAND

## Slide 8: IC Fabrication
Furnace used to oxidize (900-1200 C)
Mask exposes photoresist to light, allowing removal
HF acid etch
piranha acid etch
diffusion (gas) or ion implantation (electric field)
HF acid etch

## Slide 9: IC Fabrication
Heavy doped poly is grown with gas in furnace (chemical vapor deposition)
Masked used to pattern poly
Poly is not affected by ion implantation

## Slide 10: IC Fabrication
Metal is sputtered (with vapor) and plasma etched from mask

## Slide 11: Cell Library (Snap Together)
Layout

## Slide 12: Synthesized and P&R’ed MIPS Architecture

## Slide 13: Feature Size
Shrink minimum feature size…
  Smaller L decreases carrier time and increases current
  Therefore, W may also be reduced for fixed current
  Cg, Cs, and Cd are reduced
  Transistor switches faster (~linear relationship)

## Slide 14: Minimum Feature Size
Year | Processor | Speed | Process
1982 | i286 | 6 - 25 MHz | 1.5 mm
1986 | i386 | 16 – 40 MHz | 1.5 - 1 mm
1989 | i486 | 16 - 133 MHz | .8 mm
1993 | Pentium | 60 - 300 MHz | .6 - .25 mm
1995 | Pentium Pro | 150 - 200 MHz | .5 - .35 mm
1997 | Pentium II | 233 - 450 MHz | .35 - .25 mm
1999 | Pentium III | 450 – 1400 MHz | .25 - .13 mm
2000 | Pentium 4 | 1.3 – 3.8 GHz | .18 - .065 mm
2005 | Pentium D | 2.66 – 3.6 GHz | .09 - .065 mm
2006 | Core 2 | 1.06 – 3 GHz | .065 mm
Upcoming milestones:
45 nm (Xeon 5400 Nov. 2007),
32 nm (2009-2010), 22 nm (2011-2012), 16 nm (2013)

## Slide 15: Integration Density Trends (Moore’s Law)
Pentium Core 2 Duo (2007) has ~300M transistors

## Slide 16: Microarchitectural Parallelism
Parallelism => perform multiple operations simultaneously
  Instruction-level parallelism
    Execute multiple instructions at the same time
    Multiple issue
    Out-of-order execution
    Speculation
  Chip multiprocessing
    Execute multiple threads at the same time on one CPU
    Execute multiple threads at the same time on multiple processors