## Slide 1: An Integrated Reduction Technique for a Double Precision Accumulator
Krishna Nagar, Yan Zhang, Jason Bakos
Dept. of Computer Science and Engineering
University of South Carolina

## Slide 2: Double Precision Accumulation
Many kernels targeted for acceleration include
For large datasets, values delivered serially to an accumulator
A,
set 1
Σ
B,
set 1
C,
set 1
D,
set 2
E,
set 2
F,
set 2
G,
set 3
A+B+C,
set 1
D+E+F,
set 2
H,
set 3
I,
set 3
G+H+I,
set 3

## Slide 3: The Reduction Problem
+
Mem
Mem
Control
Partial sums

## Slide 4: Reduction-Based Accumulator: Previous Work
Paper | # d.p. adder IP (~1000 slices/ea) | Reduc’n Logic | Reduc’n BRAM | # DSP48 | D.p. adder speed | Accumulator speed | Out-of-order outputs
Prasanna DSA ’07 (Virtex 2P) | 2 | 2215 slices | 3 | n/a | 170 MHz | 142 MHz | Yes
Prasanna SSA ’07 (Virtex 2P) | 1 | 1804 slices | 6 | n/a | 170 MHz | 165 MHz | Yes
Gerards ’08 (Virtex 4) | 1 | 2722 slices | 9 | 3 (from d.p. adder) | 324 MHz | 200 MHz | No
This work (Virtex 5) | 0 | < 1000 slices | 0 | 3 | 355 MHz | 300+ MHz | No

## Slide 5: Approach
Reduction complexity scales with the latency of the core operation
  Reduce latency of double precision add?
IEEE 754 adder pipeline (assume 4-bit significand):
Compare exponents
Add 53-bit mantissas
De-normalize smaller value
Round
Re-normalize
1.1011 x 223
1.1110 x 221
1.1011 x 223
0.01111 x 223
10.00101 x 223
10.0011 x 223
1.00011 x 224
Round
1.0010 x 224

## Slide 6: Adder Pipeline
Mantissa addition
  Cascaded, pipelined DSP48 adders
  Scales well, operates fast
De-normalize
  Exponent comparison and a variable shift of one significand
  Xilinx IP uses a DSP48 for the 11-bit comparison (waste)

## Slide 7: Base Conversion
Previous work in s.p. MAC designs base conversion
  Idea:
    Shift both inputs to the left by amout specified in low-order bits of exponents
    Reduces size of exponent, requires wider adder
Example:
  Base-8 conversion:
    1.01011101, exp=10110 (1.36328125 x 222 => ~5.7 million)
    Shift to the left by 6 bits…
    1010111.01, exp=10 (87.25 x 28*2 = > ~5.7 million)

## Slide 8: Exponent Compare vs. Adder Width
Base | Exponent Width | Denormalize speed | Adder Width | #DSP48s
16 | 7 | 119 MHz | 54 | 2
32 | 6 | 246 MHz | 86 | 2
64 | 5 | 368 MHz | 118 | 3
128 | 4 | 372 MHz | 182 | 4
256 | 3 | 494 MHz | 310 | 7
denorm
DSP48
DSP48
DSP48
renorm

## Slide 9: Accumulator Design

## Slide 10: Three-Stage Reduction Architecture
“Adder” pipeline
Input
buffer
Output
buffer
Input

## Slide 11: Three-Stage Reduction Architecture
“Adder” pipeline
Input
buffer
Output
buffer
a3
a2
a1
B1
Input
0

## Slide 12: Three-Stage Reduction Architecture
“Adder” pipeline
Input
buffer
Output
buffer
a3
a2
a1
B2
Input
B1

## Slide 13: Three-Stage Reduction Architecture
“Adder” pipeline
Input
buffer
Output
buffer
B1
a3
B2
Input
a1+a2
B3

## Slide 14: Three-Stage Reduction Architecture
“Adder” pipeline
Input
buffer
Output
buffer
B1
a3
Input
a1+a2
B4
B2+B3

## Slide 15: Three-Stage Reduction Architecture
“Adder” pipeline
Input
buffer
Output
buffer
a3
Input
a1+a2
B5
B2+B3
B1+B4

## Slide 16: Three-Stage Reduction Architecture
“Adder” pipeline
Input
buffer
Output
buffer
Input
a1+a2+a3
B6
B2+B3
B1+B4
B5

## Slide 17: Three-Stage Reduction Architecture
“Adder” pipeline
Input
buffer
Output
buffer
Input
a1+a2+a3
B7
B2+B3+B6
B1+B4
B5

## Slide 18: Three-Stage Reduction Architecture
“Adder” pipeline
Input
buffer
Output
buffer
Input
a1+a2+a3
B8
B2+B3+B6
B1+B4+B7
B5

## Slide 19: Three-Stage Reduction Architecture
“Adder” pipeline
Input
buffer
Output
buffer
Input
C1
B2+B3+B6
B1+B4+B7
B5+B8
0

## Slide 20: Minimum Set Size
Four “configurations”:
Deterministic control sequence, triggered by set change:
  D, A, C, B, A, B, B, C, B/D
Minimum set size is 8

## Slide 21: Use Case: Sparse Matrix-Vector Multiply
A
0
0
0
B
0
0
0
0
C
0
D
E
0
0
0
F
G
H
0
0
0
0
0
0
0
I
0
J
0
0
0
0
K
0
0
val
col
ptr
A
B
C
D
E
F
G
H
I
J
K
0
4
3
5
0
4
5
0
2
4
3
0
2
4
7
8
10
11
0
1
2
3
4
5
6
7
8
9
10
(A,0) (B,4) (0,0) (C,3) (D,4) (0,0)…
Group vol/col
Zero-terminate

## Slide 22: SpMV Architecture
Enough memory bandwidth to read:
  5 val/col pairs (80 x 5 bits) per cycle
  ~15-20 GB/s
Requires minimum number of entries per row:
  5 x 8 = 40
  Many sparse matrices don’t have this many values per row
  Zero padding will degrade performance for many matrices

## Slide 23: New SpMV Architecture
Delete tree, replicate accumulator, schedule matrix data:
val0,0 | col0,0 | val1,0 | col1,0 | val2,0 | col2,0 | val3,0 | col3,0 | val4,0 | col4,0
val0,1 | col0,1 | val1,1 | col1,1 | val2,1 | col2,1 | val3,1 | col3,1 | val4,1 | col4,1
val0,2 | col0,2 | val1,2 | col1,2 | val2,2 | col2,2 | val3,2 | col3,2 | val4,2 | col4,2
val0,3 | col0,3 | val1,3 | col1,3 | val2,3 | col2,3 | val3,3 | col3,3 | val4,3 | col4,3
val0,4 | col0,4 | val1,4 | col1,4 | val2,4 | col2,4 | val3,4 | col3,4 | val4,4 | col4,4
val0,5 | col0,5 | val1,5 | col1,5 | val2,5 | col2,5 | val3,5 | col3,5 | val4,5 | col4,5
val0,6 | col0,6 | 0.0 | 0.0 | val2,6 | col2,6 | val3,6 | col3,6 | val4,6 | col4,6
val0,7 | col0,7 | 0.0 | 5 | val2,7 | col2,7 | val3,7 | col3,7 | val4,7 | col4,7
val0,8 | col0,8 | val5,0 | col5,0 | val2,8 | col2,8 | val3,8 | col3,8 | val4,8 | col4,8
400 bits

## Slide 24: Performance Results

## Slide 25: Conclusions
Developed serially-delivered accumulator using base-conversion technique
Limited to shallow pipelines
  Deeper pipelines require large minimum set size
    4 -> 11, 5 -> 19, 6 -> 23
Goal: new reduction circuit to support deeper pipelines with no minimum set size
Acknowledgements:
  NSF awards CCF-0844951, CCF-0915608