## Slide 1: Next Generation Interconnection Technology for High-Performance Computer Systems
Jason D. Bakos
Department of Computer Science
University of Pittsburgh

## Slide 2: Talk Outline
Brief introduction to system interconnection technology
  Examples
  Challenges
  Electrical and optoelectronic signaling
High-performance interconnection technology research at Pitt
  Optoelectronic Multi-Chip Modules (OE-MCM)
  Multi-Bit Differential Signaling (MBDS)
Dissertation research
  Lightweight Hierarchical Error Control Codes (LHECC)

## Slide 3: System Interconnect
Network-on-chip
Printed circuit boards
Multi-Chip Modules
Backplanes
Peripherals
System-level interconnect
  Short-haul
  High-performance

## Slide 4: Challenges for System Interconnect
Signal integrity
  Capacitance/inductance
  Noise
  Timing/jitter
Area
  I/O pads precious
  Driver size
Packaged chip
Packaged chip
Source: Intel Corporation

## Slide 5: Electrical Signaling
Single-ended
  1 wire per bit
  Disadvantages
    Requires shared reference
    Susceptible to noise
    Switching noise
Differential (LVDS)
  2 wires per bit
  Data encoded as {01} or {10}
  Advantages
    Large GDP
    EM coupled transmission lines
    Low switching noise
    Low noise => low voltage swing
  Disadvantages
    Wasteful in I/O pads

## Slide 6: Optoelectronic Signaling
Optical signaling
  Used in long-haul signaling
Chip-level optical signaling
  Dense high-speed channel arrays
  Orthogonal to die
  OE conversion
Vertical Cavity Surface Emitting Lasers (VCSEL)
  Gallium-Arsenide (GaAs)
    “direct-bandgap”
High-speed photodetectors
  GaAs
Issues:
  Packaging
  Manufacturability
GaAs die
area pads
Top-emitting laser
GaAs die
area pads
Incoming laser
driver circuitry
VCSEL array
flip-chip bonds
receiver circuitry
photodetector array

## Slide 7: Optoelectronic Architectures
“Free Space”
“Guided Wave”
PCB
Si die
VCSEL
Si die
photodetector
waveguide
PCB
Si die
VCSEL
microlens
Si die
mirror
photodetector

## Slide 8: Talk Outline
Brief introduction to system interconnection technology
  Examples
  Challenges
  Electrical and optoelectronic signaling
High-performance interconnection technology research at Pitt
  Optoelectronic Multi-Chip Modules (OE-MCM)
  Multi-Bit Differential Signaling (MBDS)
Dissertation research
  Lightweight Hierarchical Error Control Codes (LHECC)

## Slide 9: OE Conversion Technology
Area pads
Window
VCSEL site
Passive alignment mark

## Slide 10: OE Crossbar Switch Chip

## Slide 11: OE Interconnect using Fiber Image Guides
Top
Bottom
Side
Dense lattice of fiber cores
5-20 um diameter, 2K-15K cores/mm2

## Slide 12: OE-MCM Demonstrator
Chip 2
Chip 3
Chip 1
Chip 2
Chip 3
IN
OUT
Chip 1

## Slide 13: Multi-Bit Differential Signaling (MBDS)
Differential (LVDS) channel
Current-mode drivers
Data encoded as
  {01} or {10}
Advantages
  Low switching noise
  Large GDP
  Coupled transmission lines
  Low noise => low voltage swing
Disadvantages
  Two connections for each bit
  Wasteful in I/O pads
Multi-Bit Differential (MBDS) channel
Data encoded with fixed number of ones
“N-choose-M (nCm)” symbols
  {0011}, {0101}, {0110}, {1001}, {1010}, {1100}
Advantages
  Same noise rejection as differential
  Higher information capacity

## Slide 14: “N choose M (nCm)” Encoding
Code set size
Effective bits
EXAMPLE
6-wire MBDS channel
code size = 20 codes
effective bits = 4
equivalent to 8-wire differential channel
25% fewer pads (8 versus 6)
25% less power (4 1-bits on versus 3)

## Slide 15: MBDS Test Chip
Test setup
.5 um SiGe chip implementing
2, 4, 6, 8-wide MBDS drivers and receivers
Test board with 8” channels
MBDS -> MBDS receivers
MBDS -> commercial LVDS receivers
Tested at 700 Mb/s

## Slide 16: Talk Outline
Brief introduction to system interconnection technology
  Examples
  Challenges
  Electrical and optoelectronic signaling
High-performance interconnection technology research at Pitt
  Optoelectronic Multi-Chip Modules (OE-MCM)
  Multi-Bit Differential Signaling (MBDS)
Dissertation research
  Lightweight Hierarchical Error Control Codes (LHECC)

## Slide 17: Error Correction Codes
Error correction codes used to increase signal integrity
  Noisy communication channels
    Ex: wired/wireless signaling, storage mediums
Examples:
  Cellular networks, deep-space signaling, digital TV/HDTV transmission, hard/optical disks
ECC codes require information overhead
  Acceptable for very noisy channels
  Minimize by applying code over large blocks of data
  Examples:
    11 bytes for hard disks, 187 bytes for HDTV

## Slide 18: ECC Introduction
ECC encoding over large blocks requires
  Memory
  Computation
Encoding/decoding performed using software or dedicated ASICs
  Decoding performed at low speeds (megabits at most)
Traditional ECC techniques not practical for off-chip interfaces
  Memory, real estate
Need new class of ECC code for system interconnect
  Encode/decode with small space
  Small block size
  Low overhead
  Possible with MBDS signaling?

## Slide 19: nCm Encoding: Inherent Error Detection
Most types of bit errors can be detected at receiver
0011
1011
0111
0001
0010
1101
1110
1000
0100
1 error
3 errors
Odd-number of bit errors
Even-number of bit errors
0011
1111
1001
1010
0101
0110
0000
2 errors

## Slide 20: nCm Encoding: Inherent Error Detection
Channel | P(detect 2-bit error) | P(detect 4-bit error) | P(detect 6-bit error)
4c2 | 33% |  | 
6c3 | 40% | 40% | 
8c4 | 43% | 49% | 43%

## Slide 21: nCm Encoding: Unused Code Space
Each nCm code set has unmapped code words
Use this to offset overhead required for error control
0011
0101
0110
1001
1010
1100
00
01
10
11
?
?
4c2 symbol set => binary value
4c2
4c2
36 combinations
5 bits
2 bits
2 bits
6 cw
6 cw
Use multiple MBDS channels in parallel
Do not use nCm symbols that are counteractive to ECC
Req’d number of channels for extra bit

## Slide 22: Need for Error Control Coding
Single or multiple bit errors in nCm symbols invalidates entire corresponding binary message
Some types of errors fool receivers
Need error control code that:
  Works over nCm-encoded channels
  Uses properties of nCm channel code to minimize overhead
Solution:
  Encode data over parallel MBDS channels
  Establish rules governing nCm symbols selected to encode data
00110011
6 bits
00111011
????

## Slide 23: Hierarchical Encoding
Raw binary data
Symbolic ECC block
Code word over parallel MBDS channels
start with raw binary data
Encode portion of data, set rules for nCm symbol selection
Encode remainder of data using nCm symbols
high-level code
low-level code
Use nCm symbols to build code set which conforms to binary distance for ECC

## Slide 24: Low-Level Code
nCm code sets have distance=2
t = floor((d-1)/2)
Set new distance by partitioning into equal-size subsets
  Maximize number of symbols/subset
0011
0101
1010
1001
0110
1100
Example:
4c2, distance=4
Subsets:
  0 => {0011, 1100}
  1 => {0101, 1010}
  2 => {0110, 1001}
If subset is known, bit errors may be corrected
  Example: 0111, subset=2
  Correct to 0110

## Slide 25: High-Level Code: Linear Block Codes
k data symbols
n-k parity symbols
block size=n
Can correct:
erasures
errors
Checksum
  Requires 1 parity symbol
  Can correct 1 erasure
Near-MDS code
  Corrects erasures:
    Number of parity symbols - 1
  Corrects errors:
    (Number of parity symbols – 1) / 2
  Restrictions:
    Symbol base must be prime or power of a prime
    If symbol base = pm, max block size = pm+1 - 1
MDS code (Reed-Solomon)
  Can correct erasures:
    Number of parity symbols
  Can correct errors:
    Number of parity symbols / 2
  Restrictions:
    Symbol base must be prime or power of a prime
    Max block size = symbol base + 1

## Slide 26: Encoding LHECC
0101001001
0010010100
(s-data)
(c-data)
01010010010010010100
b bits
Parity symbols
Data symbols
base conv. 2->s
Data as nCm symbols
Parity as nCm symbols
base conv. 2->c

## Slide 27: Example #1: Encoding
Encode 101…
2
1
0
1
0
1
bit
grp.
Assume 3 x 4c2 channels
  Low level
    s=3, c=2
  High level
    (3,2) checksum code
  s-data
    sk = 9 cw (3 bits)
  c-data
    cn = 8 cw (3 bits)
  code rate = 6 bits / 12 wires
    “Free” ECC
Encode 111101…
2
1
1112 = 213
2
1
0
Compute checksum parity…
1001
0101
1100

## Slide 28: Example #1: Decoding
Assume bit error occurs…
X + 1 = 0 (mod 3), X = 2
Symbol in error must be 0110 or 1001
  dist(1101,0110) = 3, dist(1101,1001) = 1
  Corrected symbol is 1001
Decoder:
  If invalid code word is detected
    Determine subset
    Use minimum distance decoder
1001
0101
1100
1101
0101
1100
?
1
0
2
1
0
grp.
cw

## Slide 29: LHECC Advantages
LHECC codes provide correction and additional detection to MBDS links
LHECC codes are lightweight:
  Parity symbols in high-level only consume portion of nCm symbol data
  Requires less parity symbols in high-level code (vs. traditional codes)
  Takes advantage of inherent properties of nCm channel code
LHECC encoders/decoders require only a few hundred logic gates
  Pipelined and operate at core speed
encoder
binary
MBDS driver
MBDS driver
MBDS driver
MBDS receiver
decoder
binary
MBDS receiver
MBDS receiver

## Slide 30: Link Modeling
encoded code words
(CMOS digital)
encoded code words out (100K load)
Driver input
Receiver output
Input is sampled at midpoint
Outputs sampled at t(input) + latency
cwn
cwn+1
cwn-1
cwn
cwn+1
cwn-1
latency
Replicated for each channel in the link
Consistent sequence of random code words transmitted

## Slide 31: Error Source Modeling
Goal: Capture link behavior in the presence of modeled error sources
Determine relative error results for links with and without LHECC support
Error sources from link model:
  Jitter
  Transmission line attenuation, crosstalk
  Noise from transistors
Input to receiver
Receiver output
1.8 GCW/s
2.2 GCW/s
2.6 GCW/s
3.0 GCW/s
3.4 GCW/s
3.8 GCW/s
4.2 GCW/s
4.6 GCW/s

## Slide 32: Supply Noise
Add independent Vdd noise to driver and receiver
Intel: measured supply noise on a busy 1.5 V Pentium 4 processor
  17-20 mV standard deviation
To generate:
  Assume links operating at core switching frequency
  Generate white Gaussian noise
    Sampled at 20 GHz for 20 us
  Apply passband butter filter to noise, 200 MHz band centered on op. frequency
stdev=.275
stdev=.0388

## Slide 33: Fringe Capacitance in Driver
Assume layout parasitics and packaging add capacitance effects in driver current-steering legs
  Where it hurts drivers most
  Adds additional crosstalk

## Slide 34: Experimental results (no noise)
 | detects+errors |  | errors | 
 | base freq. | differential | base freq. | differential
3x4c2 | 3.8 GHz | 400 MHz | 4.2 GHz | 600 MHz
3x6c3 | 3.2 GHz | 600 MHz | 3.8 GHz | 800 MHz
3x8c4 | 2.8 GHz | 800 MHz | 3.6 GHz | 800 MHz

## Slide 35: Experimental results (supply noise)
 | detects+errors |  | errors | 
 | base freq. | differential | base freq. | differential
3x4c2 | 3.6 GHz | 400 MHz | 4.0 GHz | 600 MHz
3x6c3 | 3.0 GHz | 600 MHz | 3.6 GHz | 1 GHz
3x8c4 | 2.8 GHz | 600 MHz | 3.4 GHz | 1 GHz

## Slide 36: Experimental results (fringe capacitance)
 | detects+errors |  | errors | 
 | base freq. | differential | base freq. | differential
3x4c2 | 3.4 GHz | 400 MHz | 3.8 GHz | 600 MHz
3x6c3 | 3.0 GHz | 600 MHz | 3.6 GHz | 400 MHz
3x8c4 | 3.0 GHz | 600 MHz | 3.6 GHz | 400 GHz

## Slide 37: Conclusions
System-level interconnect
  Next-generation interconnect
    optoelectronic (high density channel arrays)
    serialized electrical using encoding techniques
LHECC over MBDS channels offers lightweight error control
  Increases signal integrity, reliability, noise immunity, and maximum transmission rate
  Utilizes small encoders and decoders