## Slide 1: OpenVX Graph Acceleration
Jesse Villarreal, Lucas Weaver, Kedar Chitnis (TI)
Jason D. Bakos and Madushan Abeysinghe (USC)
Prior work by Yang Gao (Ph.D.), Fan Zhang (Ph.D.),
Konstantin Rubin, Benjamin Morgan (B.S.) , Shaun Gause (M.S.)
Heterogeneous and Reconfigurable Computing Group

## Slide 2: Heterogeneous and Reconfigurable Computing Group
Domain-Specific Processors (FPGA, GPU, DSP)
Tools
Applications
TI collaboration since 2013
  2013-2016 (Shannon/Hawking):
    HPC and Vision applications
    DSL for auto-tuning
    Automatic scratchpad allocation
  2017-current (ADAS TDA2x):
    Computer vision

## Slide 3: HPC and Vision Applications
Shannon 45nm (8 c66x, 2012): 128 spGflops@10 Watts -> 12.8 Gflops/Watt peak
Nvidia K20x 28nm (2013): 3.95 spTflops@225 Watts -> 17.6 Gflops/Watt peak
Intel 22nm Xeon Phi 5110p: 2.12 spTflops@225 Watts -> 9.4 spTflops/Watt
i7 Ivy Bridge (22nm): 448 spGflops@77 Watts -> 5.8 spGflops/Watt
8xShannon Advantech
16xShannon Advantech
144x(Hawking+Shannon)
nCore

## Slide 4: HPC and Vision Applications
Sparse Matrix-Vector Multiply
Symmetric Sparse Matrix-Vector Multiply
  Developed tiled approach to limit slowdown to 30 to 40% vs. non-symmetric

## Slide 5: HPC and Vision Applications
Platform | C66x Shannon | CortexA9 | Intel i7-2600 | K20
Actual Gflops/ Peak Gflops | 12% | 7% | 4% | 3%
Gflops | 15.4 | 0.7 | 17.1 | 108.6
Power (W) | 5.7 | 4.8 | 52.5 | 79.0
Gflops/W | 2.69 | 0.2 | 0.3 | 1.4
Dense Lucas-Kanade Optical Flow

## Slide 6: DSL for Auto-Tuning Stencil Loops
PIA
LLVM IR
Executable
Assembly Code
Kernel | Baseline II | Optimized II | Strategy
Matrix Add | 2 | 1.5 | Unroll 2x+SIMD
1x3 Mean | 2 | 2 | 
3x3 Mean | 5 | 4.5 | Unroll 6x
Jacobi | 3 | 2.5 | Unroll 2x or 4x
Gaussian | 4 | 4 | 
Sobel | 5 | 4.25 | Unroll 8x
Harris Corner | 27 | 14 | Unroll 2x+SIMD
Lucas Kanade | 15 | 9.5 | Unroll 2x+SIMD
STENCIL(foo)
$t = A[-1,0] * @c1 +
A[0,0] * @c2 +
A[0,1] * @c3;
C = 1.0 / $t;
END
%size_x = N
loop:
%j = phi i32 [ 0, %beforeloop ], [ %next_j, %loop]
%1 = add i32 %j, %0
%I0a = getelementptr inbounds float* %I0, i32 %1
%I0v = load float* %I0a, align 4
%I1a = getelementptr inbounds float* %I1, i32 %1
%I1v = load float* %I1v, align 4
%r = fadd float %I0v, %I1v
%O0a = getelementptr inbounds float* %O0, i32 %1
store float %r, float* %O0a, align 4
%next_j= add i32 %j, 1
%2 = icmp slt i32 %next_j, %size_x
br i1 %2, label %loop label %afterloop
afterloop:
Unroll
SIMD
Align

## Slide 7: Automatic Scratchpad Allocation
Non-zeros per row | val | col | ptr | y | prod | Gflops | Norm. Perf | Note
3 | S S L2 C | L2 L2 L2 C | L2 L2 C C | L2 L2 C C | L1 L2 S C | 2.26 1.84 1.23 1.44 | 1.57 1.28 0.85 1 | Best Median Worst1 All cache
151 | L2 S C C | S C C C | L2 L2 C C | L2 L2 C C | L2 S L2 C | 3.76 3.55 2.66 2.51 | 1.50 1.41 1.06 1 | Best Median Worst1 All cache
L1:level 1 SPRAM, L2:level 2 SPRAM, S:MSMC, C:cache
1: The worst amongst the configurations with SPRAM
SpMV: 5 arrays (val, col, ptr, y, prod) and 4 allocation targets (L1S, L2S, MSMC, cache)
45=1024 possible configurations

## Slide 8: Automatic Scratchpad Allocation
, : prefetch hit, miss from XMC
(isolate specific arrays)
, : datasheet

## Slide 9: Automatic Scratchpad Allocation

## Slide 10: OpenVX/BAM on ADAS TDA2x
ADAS TDA2x: 2-core C66x @750 MHz
BAM: L2S/DMA only
OpenVX: pixel-by-pixel vision primitives
  Offloaded kernels executed sequentially
vxColorConvertNode
vxGaussian3x3Node
vxChannelExtractNode

## Slide 11: OpenVX and BAM (current work)

## Slide 12: OpenVX and BAM (current work)
(process)
(in)
(out)

## Slide 13: DMA and Scratchpad
max(compute,DMA)
processor
DMA controller
trigger
time
idle
write tile n-1 to DRAM
process tile n
idle
input ping buffer
input pong buffer
output ping buffer
output pong buffer
tile n
tile n-1
tile n+1
tile n+2
tile n+1
read tile n+1 from DRAM
trigger
process tile n+1
idle
trigger
process tile n+2
idle
write tile n to DRAM
read tile n+2 from DRAM
idle
write tile n+1 to DRAM
tile n+1
tile n+2
tile n+1
tile n
tile n+2
tile n
tile n-1
tile n
tile n-1
tile n
tile n
tile n
tile n+1
tile n
max(trigger+compute,trigger+DMA)

## Slide 14: Factor 1: Tile Size
Chart: AccumulateSquared Kernel 1600x1200 Input Image
| 32x16 | 32x24 | 64x16 | 64x24 | 64x48 | 64x64 | 128x48 | 256x24 | 320x24 | 384x16
DMA cycles | 4086042 | 3351592 | 2657840 | 2254197 | 2122940 | 2147923 | 1968607 | 2018998 | 1940477 | 2033277
Chart: AccumulateSquared Kernel 1600x1200 Input Image
| 32x16 | 32x24 | 64x16 | 64x24 | 64x48 | 64x64 | 128x48 | 256x24 | 320x24 | 384x16
DMA cycles | 4086042 | 3351592 | 2657840 | 2254197 | 2122940 | 2147923 | 1968607 | 2018998 | 1940477 | 2033277
Compute cycles | 2106936 | 1828958 | 1684803 | 1551327 | 1471052 | 1495759 | 1984855 | 2125456 | 2323605 | 2241750
1.58X
2.11X
best DMA
best compute
best max(DMA,compute)

## Slide 15: Factor 2: Scratchpad Access Pattern
vxColorConvertNode
ex. time = X
vxGaussian3x3Node
ex. time = Z
vxChannelExtractNode
ex. time = Y
DRAM -> scratchpad (C)
DRAM -> scratchpad (A)
scratchpad -> DRAM (B)
scratchpad -> DRAM (D)
DRAM -> scatchpad (E)
scatchpad -> DRAM (F)
scratchpad buffers: 2, size = scratchpad/4
time = max(C+D,Y)

## Slide 16: Factor 2: Scratchpad Access Pattern
vxColorConvertNode
ex. time = X
vxGaussian3x3Node
ex. time = Z
vxChannelExtractNode
ex. time = Y
scratchpad
DRAM -> scratchpad (A)
scratchpad
scratchpad -> DRAM (D)
DRAM -> scatchpad (E)
scatchpad -> DRAM (F)
scratchpad buffers: 3, size = scratchpad/6
time = max(A+D,(X+Y)/l)

## Slide 17: Lambda
l Values for Merged Kernels (Observed)

## Slide 18: Graph Partitioning
B6 = 203
B7 = 877
B8 = 4140
B9 = 21147
B10 = 115975
B11 = 678570
B12 = 4213597

## Slide 19: Performance Considerations
Problem:
  Group size determines:
    Number of DMA transactions
    Maximum tile size
  Tile size determines:
    DMA bandwidth
    Compute throughput
  Graph time = sum of group times
Approach:
  Train memory performance model and compute model to optimize grouping and tile size together

## Slide 20: DMA/Memory System Performance Model
Characterize:
  19 kernels (originally 35), 25 tile sizes, all possible pixel depths (per kernel)
  1460 total test cases (culled from 2819 original tests)
Features:
  input tile width, height in pixels (TIW, TIH)
  output tile width, height in pixels (TOW, TOH)
  total input, output width (tile width x pixel size x number of inputs) (TTIW, TTOW)
  total input, output size, TTIW*TIH (TIS, TOS)
  number of inputs, outputs (NI, NO)
  pixel depth (PD)
  stencil neighborhood width, height (SNW, SNH)
Best accuracy: TTIW, TIH, TTOW, TOH

## Slide 21: Curve-Fitted Memory Model

## Slide 22: Equivalence Classes
Feature combinations | #Classes/ Ave. Size | Ave. /max. stddev of class b/w | Mean error of classes
TTIW, TTOW, TIH, TOW, NI, NO, TIS, TOS | 500 2.9 | 6.7 MB/s 100 MB/s | 114 MB/s
TIW, TIH, NI, NO, TIS, TOS, SNW, SNH | 500 2.9 | 6.7 MB/s 100 MB/s | 219 MB/s
TTIW, TIH, TTOW, TOH | 448 3.3 | 17 MB/s 340 MB/s | 100 MB/s

## Slide 23: Performance Models
DMA: linear interpolant model of DMA b/w
  Find nearest 5 observations
    Calculate weights
    Calculate weighted average
  RMS training error = 32 MB/s
  RMS testing error = 248 MB/s
  Range = 189 MB/s to 4.33 GB/s
Compute: lookup kernel names and nearest tile WxH prod
616 MB/s
in_width=16,
out_width=8,
in_height=48,
out_height=48
in_width=16,
out_width=14,
in_height=48,
out_height=46
in_width=16,
out_width=10,
in_height=48,
out_height=42
in_width=16,
out_width=16,
in_height=48,
out_height=48
in_width=8,
out_width=8,
in_height=48,
out_height=48
in_width=8,
out_width=6,
in_height=48,
out_height=46
6.3
6.3
8.0
8.0
8.5
w=.23
w=.23
w=.18
w=.18
w=.17
723 MB/s
742 MB/s
423 MB/s
356 MB/s

## Slide 24: Model Accuracy and Performance
0.25 cycles/pixel (compute)
0.13 cycles/pixel
(compute)
0.44 cycles/pixel
(compute)
Compute bound:
0.81 cycles/pixel
DMA bound:
3 x 1600x1200x1 DMA @ 4.33 GB/s @ 750 MHz
0.48 cycles/pixel

## Slide 25: Impact of Tile Size on Merged Kernels
1.71

## Slide 26: Speedups
Predicted Speedups
Actual Speedups

## Slide 27: Model Accuracy

## Slide 28: Randomly Generated Graphs
For each graph
  For each grouping
    For each allocable tile size (constrained by scratchpad capacity)…
      Find predicted speedup (vs individual nodes with 64x48 tiles)

## Slide 29: Speedup Distribution
Speedups above 1.5 = 0.95%
Speedups between 1 and 1.5 = 30.74%
Speedups below 1 = 68.30%

## Slide 30: Compute/DMA Makeup

## Slide 31: Impact of Tile Size
Total time for 128x48 = 9.47 ms
Group 1 DMA for 128x96 = 1.63 ms
Group 2 compute for 160x48 = 7.37 ms
Total time = 1.63 + 7.37 =9.00 ms

## Slide 32: Current Work
B
E
vxNot
vxAdd
vxNot
Executed code:
for (i=[pixel in A])
C[i]=not A[i]
for (i=[pixel in B])
D[i]=not B[i]
for (i=[pixel in C])
E[i]=C[i]+D[i]
Requires 2 intermediate buffers C, D
Each loop achieves low IPC
A
C
D
Ideal code:
for (i=[pixel in A]) {
temp1=not A[i];
temp2=not B[i];
E[i] = temp1+temp2;
}
No intermediate buffers
Loop achieves higher IPC

## Slide 33
Thank you!